## Slide 1: Introduction to Signals in Mechatronics
Akbar Q

## Slide 2: Introduction
Signals are the backbone of mechatronic systems. They facilitate communication between components such as sensors, actuators, and controllers. Understanding signals is crucial for designing and troubleshooting these systems.

## Slide 3: Basic Types
Analog Signals
Digital Signals

## Slide 4: Primary Classification
ANALOG
- Continuous in nature.
- Represented by varying values over time (e.g., temperature readings).
- Examples: Voltage, current, pressure.
DIGITAL
- Discrete and binary in nature (0s and 1s).
- Used for precise control and communication.
- Examples: Data transmission, microcontroller inputs/outputs.

## Slide 5: Digital Does NOT Mean 2 Levels
It can have more levels, just have to be discrete levels

## Slide 6: Discrete Levels

## Slide 7: Week 1 Activity 1
Find Out 5 Signals and Identify if they are Digital or Analog

## Slide 8: Analog Signals
Advantages
- Simplicity: Easy to generate and detect.
- Precision: Can represent a wide range of values with high resolution.
- Existing Infrastructure: Widespread use in legacy systems.
Disadvantages
- Noise Susceptibility: Vulnerable to electromagnetic interference (EMI).
- Drift and Offset: Signal degradation over time or distance.
Complexity in Processing: Requires additional circuitry for accurate measurement.
Complexity in Generation: Requires additional circuitry for accurate timing.

## Slide 9: Generating an Analog Signal using PWM

## Slide 10: Generating an Analog Signal using PWM - Filter Circuit

## Slide 11: Result of Filtered PWM Signal

## Slide 12: Result of Filtered PWM Signal Visualized

## Slide 13: Generating an Analog Signal via a DAC

## Slide 14: Generating an Analog Signal via a DAC

## Slide 15: Many Controllers Come with DACs

## Slide 16: Measuring the Analog Signals

## Slide 17: Analog Sampling Precision

## Slide 18: Error Introduced from Quantization

## Slide 19: Interpolation is Done to Fill in Gaps

## Slide 20: Noise Pickup can Cause Bad Readings

## Slide 21: Controllers will have to Clean Up Signals

## Slide 22: FFT Can Reveal Noise/Signal Content

## Slide 23: FFT Splits the Frequency Content

## Slide 24: Every Signal Can be Broken Down

## Slide 25: Digital Signals
Advantages
- Immunity to Noise: Resistant to EMI, ensuring reliable communication.
- Ease of Data Handling: Facilitates data processing and storage.
- Precision: Reduces errors through binary representation.
Disadvantages
- Limited Resolution: Limited by the number of bits used to represent values.
- Latency Issues: Delays can occur due to processing requirements.
- EMI: High Data Rates can Cause Excessive EMI emissions

## Slide 26: Digital Signals are Noise Resistant

## Slide 27: As Long as It is With-In Limits

## Slide 28: Not Everything can Process Analog Signals but (almost) everything can Digital

## Slide 29: Typical Digital Data Used for Communication

## Slide 30: Everything is an Antenna if the Frequency is High Enough

## Slide 31: A Perfect Square Wave has Infinite Number of Harmonics – Thus It will Radiate Energy Always

## Slide 32: Directly Depends on Rise Time

## Slide 33: Varying the Number of Harmonics

## Slide 34: Varying the Number of Harmonics

## Slide 35: Inductors and Capacitors Used to Control Edge Rate and Noise

## Slide 36: Week 1 Activity 2
Find Out the Speed of 2 Common Communication Protocols

## Slide 37: The End of Week 1

## Slide 38: Chart
Chart: 
| Category 1 | Category 2 | Category 3 | Category 4
Series 1 | 4.3 | 2.5 | 3.5 | 4.5
Series 2 | 2.4 | 4.4 | 1.8 | 2.8
Series 3 | 2 | 2 | 3 | 5

## Slide 39: Table
 | Category 1 | Category 2 | Category 3 | Category 4
Item 1 | 4.5 | 2.3 | 1.7 | 5
Item 2 | 3.2 | 5.1 | 4.4 | 3
Item 3 | 2.1 | 1.7 | 2.5 | 2.8
Item 4 | 4.5 | 2.2 | 1.7 | 7

## Slide 40: Team
Name
Title
Name
Title
Name
Title
Name
Title

## Slide 41: Timeline
Title
To start a presentation, go to the Slide Show tab, and select From Beginning.
Title
To display Presenter view, in Slide Show view, on the control bar at the bottom left select the three dots, and then Show Presenter View.
Title
During your presentation, the speaker notes are visible on your monitor, but aren't visible to the audience.
Title
Title
If you can’t see the Notes pane or it is completely minimised, click Notes on the task bar across the bottom of the PowerPoint window.
The Notes pane is a box that appears below each slide. Tap it to add notes.

## Slide 42: Content
Subtitle
Add text, images, art, and videos.
Add transitions, animations, and motion.
Save to OneDrive, to get to your presentations from your computer, tablet, or phone.
Subtitle
Open the Design Ideas pane for instant slide makeovers.
When we have design ideas, we’ll show them to you right there.

## Slide 43: Content 2
Subtitle
Add text, images, art, and videos.
Add transitions, animations, and motion.
Save to OneDrive, to get to your presentations from your computer, tablet, or phone.
Open the Design Ideas pane for instant slide makeovers.
When we have design ideas, we’ll show them to you right there.
subtitle
Add text, images, art, and videos.
Add transitions, animations, and motion.
Save to OneDrive, to get to your presentations from your computer, tablet, or phone.
Open the Design Ideas pane for instant slide makeovers.
When we have design ideas, we’ll show them to you right there.
subtitle
Add text, images, art, and videos.
Add transitions, animations, and motion.
Save to OneDrive, to get to your presentations from your computer, tablet, or phone.
Open the Design Ideas pane for instant slide makeovers.
When we have design ideas, we’ll show them to you right there.

## Slide 44: Summary
With PowerPoint, you can create presentations and share your work with others, wherever they are. Type the text you want here to get started. You can also add images, art, and videos on this template. Save to OneDrive and access your presentations from your computer, tablet, or phone.

## Slide 45: Thank You
Presenter name
Email address
Website address