## Slide 1: Fundamentals of Signal Processing: Analog and Digital Techniques
Akbar Q – Calander Week 5Mechatronics Engineering Year 1

## Slide 2: Introduction to Signal Processing
Definition of Signal Processing
Importance of Signal Processing in Real-World Applications (e.g., audio, communication, medical devices, etc.)
Overview of Analog vs. Digital Signal Processing

## Slide 3: Analog Signal Processing Overview
Filters
Amplifiers
Attenuators

## Slide 7: FILTERS IN ANALOG SIGNAL PROCESSING
Types of Filters:
Low-Pass Filters (LPF)
High-Pass Filters (HPF)
Band-Pass Filters (BPF)
Band-Stop (Notch) Filters

## Slide 11: Low pass and high pass formula

## Slide 12: -3db is when power output is half

## Slide 13: Power halves
Power is Voltage x Current

## Slide 15: Impedance mismatch
Impedance of the filter is difficult to control with a passive filter
Active Filters can be Used to Increase Current Drive
Also to control impedance

## Slide 16: We need to recover losses

## Slide 18: Unity Voltage Gain Mode

## Slide 19: Why is unity voltage gain useful?
Increases Current Drive at the Output
Decouples the Load Current from Sensitive Source
Maintains the Same Signal Shape

## Slide 20: Sometimes the voltage needs to be reduced
Scales down voltage to fit within ADC range
Eg, the ESP32 can measure upto 1.1V without internal dividers but with a 1:10 division it could measure much higher voltage like 24V

## Slide 21: Opamps can be used for attenuation given the signal fits within the opamp supply voltage rails

## Slide 22: Caveats of Using Op-Amps in Real-World Signal Processing 1
Input Offset Voltage:
Small voltage difference between the inverting and non-inverting inputs.
Causes DC error in the output, especially in high-gain applications.
Requires external trimming or offset nulling circuits.
Input Bias Current:
Small current flowing into the input terminals.
Can cause voltage drops across input resistors, leading to errors.
Critical in high-impedance circuits.
Input Offset Current:
Difference between the bias currents of the two input terminals.
Exacerbates errors in precision applications.

## Slide 23: Caveats of Using Op-Amps in Real-World Signal Processing 2
Limited Bandwidth:
Op-amps have a finite gain-bandwidth product (GBW).
High-frequency signals may experience attenuation or phase shift.
Slew Rate Limitation:
Maximum rate of change of the output voltage.
Limits the op-amp’s ability to handle fast-changing signals, causing distortion.
Non-Rail-to-Rail Operation:
Many op-amps cannot swing their output voltage to the supply rails.
Reduces dynamic range, especially in low-voltage applications.
Power Supply Limitations:
Op-amps require stable and clean power supplies.
Noise or fluctuations in the supply can affect performance.

## Slide 24: Caveats of Using Op-Amps in Real-World Signal Processing 3
Temperature Sensitivity:
Parameters like offset voltage, bias current, and gain vary with temperature.
Requires careful design for temperature-critical applications.
Common-Mode Rejection Ratio (CMRR) Limitations:
Op-amps may not perfectly reject common-mode signals.
Can introduce errors in differential amplification.
Output Impedance:
Non-zero output impedance can affect signal integrity.
May require buffering for low-impedance loads.

## Slide 25: Instrumentation amplifiers are designed to overcome generic opamp caveats

## Slide 26: What is an Instrumentation Amplifier?
A specialized type of differential amplifier with:
  High input impedance
  High common-mode rejection ratio (CMRR)
  Precise gain control
Typically built using 3 op-amps or integrated as a single IC.

## Slide 27: Key Advantages of Instrumentation Amplifiers
High Input Impedance:
Minimizes loading effects on the signal source.
Fixes issues caused by input bias current in standard op-amps.
High Common-Mode Rejection Ratio (CMRR):
Effectively rejects common-mode noise and interference.
Solves problems with common-mode signals in standard op-amps.
Precise Differential Amplification:
Amplifies only the difference between two input signals.
Reduces errors caused by input offset voltage and current.
Adjustable Gain:
Gain is set using a single external resistor.
Provides better control and accuracy compared to standard op-amp configurations.

## Slide 28: Key Advantages of Instrumentation Amplifiers
High Input Impedance:
Minimizes loading effects on the signal source.
Fixes issues caused by input bias current in standard op-amps.
High Common-Mode Rejection Ratio (CMRR):
Effectively rejects common-mode noise and interference.
Solves problems with common-mode signals in standard op-amps.
Precise Differential Amplification:
Amplifies only the difference between two input signals.
Reduces errors caused by input offset voltage and current.
Adjustable Gain:
Gain is set using a single external resistor.
Provides better control and accuracy compared to standard op-amp configurations.

## Slide 29: Key Advantages of Instrumentation Amplifiers
Low Output Impedance:
Provides a strong, low-impedance output signal.
Eliminates the need for additional buffering.
Low DC Offset and Drift:
Designed for precision applications with minimal offset voltage and drift.
Reduces errors in DC and low-frequency signal processing.
Improved Noise Performance:
Lower internal noise compared to standard op-amps.
Ideal for low-noise applications like medical devices and sensors.
Rail-to-Rail Operation (in some models):
Modern in-amps can operate close to the supply rails.
Addresses the limited dynamic range of standard op-amps.

## Slide 30: Applications of Instrumentation Amplifiers
Sensor Signal Conditioning:
  Amplifies weak signals from sensors (e.g., thermocouples, strain gauges).
Medical Devices:
  Used in ECG, EEG, and other biomedical instruments.
Industrial Systems:
  Noise-resistant signal processing in harsh environments.
Precision Measurement:
  High-accuracy amplification for test and measurement equipment.

## Slide 31: BJT Based amplifiers, attenuators, filters are available but harder to design so not as common

## Slide 32: Introduction to Digital Signal Processing (DSP)
The method of analogue signal processing where the source signal is acquired by an ADC and then software processed before being regenerated by a DAC

## Slide 33: DSP FOR MICROPHONE AUDIO PROCESSING EXAMPLE

## Slide 34: Noise Reduction Techniques in DSP
Digital Filtering Techniques:
  Finite Impulse Response (FIR) Filters
  Infinite Impulse Response (IIR) Filters
Applications of Noise Reduction (e.g., audio processing, image processing)

## Slide 35: FIR Filter Diagram

## Slide 36: FIR Filters
Definition: FIR filters have a finite duration impulse response.
Stability: Always stable (no feedback).
Linear Phase: Symmetric coefficients ensure linear phase response.
Structure: Non-recursive (uses only input signals, no feedback).

## Slide 38: FIR Filters
Definition: IIR filters have an infinite duration impulse response.
Stability: Can be unstable if not designed properly (due to feedback).
Nonlinear Phase: Phase response is not linear.
Structure: Recursive (uses both input and output feedback).

## Slide 39: FIR vs iir Diagram

## Slide 40: Comparison
FIR Filters:
  Like reading a book from start to finish without looking back.
  Slow but steady and reliable.
IIR Filters:
  Like reading a book but constantly revisiting previous pages.
  Faster but can get confusing if not careful.

## Slide 41: Comparison
Feature | FIR Filters | IIR Filters
Feedback | No feedback (one-way). | Uses feedback (loop).
Stability | Always stable. | Can be unstable.
Speed | Slower (more calculations). | Faster (fewer calculations).
Signal Shape | Preserves shape (no distortion). | May distort shape slightly.
Best Use Case | Audio, image processing. | Real-time, low-resource systems.

## Slide 42: Oversampling and Averaging
Sampling a signal at a rate much higher than the Nyquist rate.
Reduces noise by spreading it over a wider bandwidth.
Combined with averaging to improve signal-to-noise ratio (SNR).

## Slide 45: Windowing
A technique to reduce spectral leakage in Fourier transforms.
Multiplies the signal by a window function (e.g., Hamming, Hanning).
Tapers the signal at the edges to minimize discontinuities.

## Slide 47: Frequency Bin
The frequency range and resolution on the frequency axis of a spectrum graph depends on the sampling rate and the size of the data record (the number of acquisition points).
The number of frequency points or lines or bands in the power spectrum is NRECORD/2, where NRECORD is the number of signal points captured in the time domain.

## Slide 49: Digital SIGNALS
PROCESSING AND MAKING THEM USABLE

## Slide 50: Schmitt Triggering
What is a Schmitt Trigger?
A comparator circuit with hysteresis.
Converts noisy or slow-changing signals into clean digital signals.

## Slide 51: Basic diagram

## Slide 52: How It Works:
Two threshold voltages: Upper Threshold (V₊) and Lower Threshold (V₋).
Output switches high when input exceeds V₊.
Output switches low when input falls below V₋.
Hysteresis prevents noise from causing false triggering.

## Slide 54: You can dedicated ICs

## Slide 55: Inductor Filtering for Noise
Uses inductors to block high-frequency noise while allowing DC or low-frequency signals to pass.
Inductors oppose changes in current.
High-frequency noise is attenuated, while low-frequency signals pass through.
Often used in combination with capacitors (LC filters).

## Slide 58: Capacitor Filtering for Noise
Capacitors block DC and low-frequency signals while allowing high-frequency noise to pass.
Placed in parallel with the signal path or power supply lines.

## Slide 61: Impedance Matching
Ensures maximum power transfer between two circuits by matching their impedances.
Uses transformers, resistors, or LC networks to match source and load impedances.
Prevents signal reflections and losses.

## Slide 62: Impedance issues

## Slide 63: Impedance issues

## Slide 64: Eye diagrams