## Slide 1: PLC Introduction
Akbar Q – Mechatronics Engineering Year 1 Semester 2

## Slide 2: Core Definition
A digitally operating electronic system designed for industrial environments that uses programmable memory for internal storage of user-oriented instructions to implement specific functions such as logic, sequencing, timing, counting, and arithmetic

## Slide 3: Key Characteristics
Industrial Hardening:
Conformal-coated PCBs resistant to humidity
Wide temperature range operation (-40°C to 70°C for some models)
DIN rail mounting with vibration resistance
Deterministic Operation:
Fixed scan cycle architecture
Watchdog timers for fault detection
<1ms I/O response times in high-speed applications
Modular Design:
Hot-swappable I/O modules
Fieldbus backplane communication (e.g., ControlNet, Profibus)

## Slide 6: “An Evolution from relay panels to modern PLCs”
(1968 Bedford Associates Modicon)

## Slide 8: Relay Logic In Operation _______________________________ https://youtu.be/Ia4RV3JYWGg
Notes: https://youtu.be/Ia4RV3JYWGg

## Slide 9: Microcontrollers vs PLCs - Technical Comparison

## Slide 10
Processing Architecture
PLCs: Dedicated real-time OS (e.g., VxWorks)
MCUs: General-purpose OS (e.g., FreeRTOS) or bare metal
Memory
PLCs: ECC RAM with battery backup
MCUs: Non-ECC volatile memory
Use Case Decision
When to choose PLC: Need >50 I/O points, harsh environment, safety-critical
When to choose MCU: Prototyping, cost-sensitive, space-constrained

## Slide 11: PLC Hardware
Processor Unit:
Dual/quad core CPUs (e.g., ARM Cortex-R series)
FPGA co-processors for high-speed logic
Battery-backed SRAM for program retention
Power Supply Design:
85-264VAC input range
24VDC output with <1% ripple
Redundant power supply configurations

## Slide 12: PLC Hardware
I/O Module:
  Digital Input:
Wetting current requirements (2-5mA typical)
24V DC Typical Operation
Debounce filters (hardware and software)
  Analog Input:
16-bit delta-sigma ADCs
Built-in signal conditioning (e.g., Siemens SM331)
0-10V DC and 4-20 mA Typical
This Photo by Unknown Author is licensed under CC BY-SA

## Slide 13: 4-20mA Input
Precision shunt resistor (250Ω ±0.1%)
Current-to-voltage conversion

## Slide 15
Digital Signal Path:
- Optical isolation (10kV/μs transient immunity)
- Schmitt trigger inputs
- Surge protection (TVS diodes)
Signal Integrity:
- Shielded twisted pair requirements
- Ground loop mitigation techniques
- Cable capacitance limitations

## Slide 17
Protocol Stack Architecture:
Application Layer
-----------------
Presentation Layer
-----------------
Session Layer
-----------------
Transport Layer
-----------------
Network Layer
-----------------
Data Link Layer
-----------------
Physical Layer

## Slide 18: PLC Programming

## Slide 19: PLC Programming Environment

## Slide 20: Practice Ladder Coding

## Slide 21: PLC Selection for Mechatronic Projects

## Slide 22: Delivering with impact
Keeping your audience engaged through effective techniques

## Slide 23: Delivering with confidence
Meaningful eye contact, purposeful gestures, and good posture can enhance your message and make it more memorable.

## Slide 24: Conclusion
Start with a hook and a clear purpose. Engage your audience using eye contact, storytelling, and questions. Design slides that enhance your message, not distract. And deliver with confidence.

## Slide 25: Q & A
How to handle audience questions effectively