## Slide 1: AME4064 - Week 1: Introduction to Mechatronics
Year 1 Mechanical Engineering

## Slide 2: AME4064
Week 1: Introduction to Mechatronics
From mechanical system to mechatronic system
Year 1 Mechanical Engineering
Theory, design thinking and supervised practical

## Slide 3: Today’s Route
Time | Activity
0-10 min | Welcome, challenge context and learning outcomes
10-35 min | What makes a product mechatronic?
35-55 min | Voltage, current, resistance and power
55-65 min | Worked example and readiness check
65-110 min | Practical: measure before building
110-120 min | Review, exit evidence and next week

## Slide 4: Learning Outcomes
By the end of this session, you should be able to:
identify the mechanical, electrical, sensing, control and actuation elements in a simple product;
distinguish an energy path from an information path;
state the units for voltage, current, resistance and power;
calculate power using ;
use a digital multimeter safely to measure voltage and resistance; and
build and check a low-voltage LED circuit with a current-limiting resistor.

## Slide 5: Why Mechatronics?
A mechanical product can be stronger, faster or lighter.
A mechatronic product can also:
sense its condition or surroundings;
make a decision from a rule or program;
create controlled motion;
respond consistently to a changing task; and
provide useful test data.
Question: Which of these capabilities would be valuable in a vehicle that must follow a line or stop at an obstacle?

## Slide 6: The Recurring Challenge Context
Throughout AME4064, use this mental model:
A small low-voltage vehicle or pipe-climber must move safely, respond to an input, and meet a stated requirement.
Possible requirements:
move a specified distance;
carry or pull a small load;
stop at an end position;
follow a contrasting line; or
repeat the task reliably.
The exact challenge may change. The engineering principles do not.

## Slide 7: Think-Pair-Share: Spot the Systems
For one minute, consider an automatic sliding door, a cordless drill or a robot vacuum.
With a neighbour, identify:
one structural or mechanical part;
one source of energy;
one input or sensor;
one decision-making component; and
one output or actuator.
Be ready to share one example.

## Slide 8: A Useful Definition
A mechatronic system combines:
mechanical structure and motion;
electrical energy;
electronics;
sensors and inputs;
control or decision-making; and
actuators or outputs.
It is the purposeful connection between these parts that matters, not simply putting electronics near a mechanism.

## Slide 9: From Mechanical System to Mechatronic System
Mainly mechanical | Mechatronic extension
Hand-operated trolley | Powered trolley with controlled motor
Spring door closer | Sensor-controlled automatic door
Bicycle bell | Speed sensor and warning indicator
Manual valve | Level sensor, controller and motorised valve

## Slide 10
A mechatronic system can observe a condition and change its behaviour.

## Slide 11: Six System Elements
Element | Question it answers | Vehicle example
Structure | What holds the system together? | chassis, brackets, wheels
Energy source | Where does useful energy begin? | battery or bench supply
Sensor/input | What does the system detect? | line sensor or limit switch
Controller | What decides what happens next? | microcontroller or relay logic
Actuator/output | What creates a physical response? | motor, LED or buzzer
Transmission | How is motion delivered? | gearbox, shaft and wheel

## Slide 12: The Energy Path
The energy path tells us how power reaches the part that does useful work.
Battery -> fuse/switch -> motor driver -> motor -> gearbox -> wheel -> motion
At each step, some energy is lost as heat, sound or friction.
Design question: Where would you place a fuse, and why should it be close to the battery?

## Slide 13: The Information Path
The information path tells us how the product decides what to do.
Sensor or switch -> controller -> motor driver -> motor action
Examples:
a limit switch tells a vehicle it has reached an end stop;
a light sensor tells a line follower where the track is;
a pushbutton asks a system to start or stop.
Information usually controls energy; it does not supply the motor’s power.

## Slide 14: Two Paths, One Product
Path | Carries | Typical components | Design concern
Energy | electrical and mechanical power | battery, fuse, driver, motor, gearbox | current capacity and protection
Information | a signal or instruction | switch, sensor, controller | correct voltage levels and reliable readings

## Slide 15
Important: A microcontroller output pin must not power a motor directly. A motor driver sits between the controller and motor.

## Slide 16: Block Diagrams Before Circuits
A block diagram is a fast way to communicate a system before selecting every wire and component.
For each block, ask:
What is its purpose?
What enters the block?
What leaves the block?
What could fail or become unsafe?
Use arrows to show direction of energy or information.

## Slide 17: Activity: Complete the Vehicle Diagram
Draw these blocks and connect them with labelled arrows:
battery;
fuse and switch;
controller;
motor driver;
motor and gearbox;
wheel; and
limit switch.
Then use two colours or line styles:
energy path from battery to wheel;
information path from limit switch to motor action.
Time: 5 minutes.

## Slide 18: Engineering Language and SI Units
Clear units make calculations and test data meaningful.
Quantity | Symbol | SI unit
Voltage |  | volt
Current |  | ampere
Resistance |  | ohm
Power |  | watt
Energy |  | joule
Time |  | second

## Slide 19
Always record a number and its unit.

## Slide 20: Voltage: Electrical Potential Difference
Voltage is the potential difference that can push charge through a circuit.
Measured across two points.
A 6 V battery pack has approximately 6 V between its positive and negative terminals.
Voltage is not current: a source can have voltage even when nothing is connected.
Analogy: voltage is similar to a pressure difference, but electrical circuits should be analysed with measurements and equations, not analogy alone.

## Slide 21: Current: Rate of Charge Flow
Current is the rate at which electric charge flows.
Measured through a component or branch.
Current needs a complete path around a circuit.
A component draws current according to the applied voltage and its electrical behaviour.
Current that is too high can overheat wires, damage components and drain a battery rapidly.
Current is measured in amperes (A), often milliamperes (mA):

## Slide 22: Resistance: Opposition to Current
Resistance limits current flow.
Measured in ohms ().
A resistor converts electrical energy into heat.
In an LED circuit, resistance is deliberately added to limit current.
Wires have low resistance, but never zero resistance in real systems.
For a fixed voltage, increasing resistance generally reduces current.

## Slide 23: Power: Rate of Energy Transfer
Electrical power tells us how quickly energy is being transferred.
where:
is power in watts (W);
is voltage in volts (V); and
is current in amperes (A).
Power matters when choosing batteries, fuses, wires, motor drivers and resistors.

## Slide 24: Worked Example: Motor Load
A 6 V motor circuit draws 0.20 A while running under a light load.
This is electrical input power. The useful mechanical output power will be lower because no motor or gearbox is 100% efficient.

## Slide 25: Check Your Understanding
Calculate the power for each case. Show the unit.
Voltage | Current | Power
5 V | 0.10 A | ?
9 V | 0.05 A | ?
12 V | 0.50 A | ?

## Slide 26
Discuss: which circuit transfers energy fastest?
Time: 3 minutes.

## Slide 27: Answers and Meaning
Voltage | Current | Power
5 V | 0.10 A | 0.50 W
9 V | 0.05 A | 0.45 W
12 V | 0.50 A | 6.0 W

## Slide 28
The 12 V, 0.50 A circuit has the highest power. It may need a larger power source, more robust wiring and a suitable protective device.

## Slide 29: Safety Gate: Low Voltage Still Needs Care
Today uses protected low-voltage DC supplies only. Even so:
inspect leads and insulation before use;
keep the bench dry, tidy and free of loose metal objects;
turn power off before changing wiring;
never deliberately short a supply or battery;
use the correct meter terminals and range;
ask the tutor if a component becomes hot, smells unusual or behaves unexpectedly.
Stop condition: disconnect power immediately if a wire, component or battery becomes hot.

## Slide 30: The Digital Multimeter (DMM)
A multimeter can measure several quantities. It is useful only when connected correctly.
Typical terminals:
COM: common (black lead);
V ohm: voltage, resistance and low-current measurements (red lead);
A or mA: current measurement terminal (red lead when instructed).
Always check the lead position before making a measurement.

## Slide 31: Measuring Voltage Safely
To measure voltage:
insert black lead into COM and red lead into V ohm;
select DC voltage mode and a suitable range;
place probes across the supply or component;
read the value and record its unit.
Never use the current terminal to measure voltage across a supply: it can create a short circuit.

## Slide 32: Measuring Resistance Safely
To measure resistance:
ensure the component is disconnected from power;
insert black lead into COM and red lead into V ohm;
select resistance mode (ohms);
touch probes to either end of the resistor;
compare measured value with the colour code or labelled value.
Resistance readings in a powered circuit are not valid and may damage the meter.

## Slide 33: Measuring Current: Tutor Demonstration
Current must be measured in series with the circuit.
break the circuit and insert the meter into the current path;
move the red lead to the correct current terminal;
start on a safe high-current range if uncertain;
return the lead to V ohm after the measurement.
For today’s practical, measure voltage and resistance independently. Do not measure current unless the tutor has checked the circuit and meter setup.

## Slide 34: The LED Needs Protection
An LED is a diode: it conducts mainly in one direction and emits light when current flows.
Long leg normally indicates the anode (+).
Short leg or flat edge normally indicates the cathode (-).
LEDs need a series resistor to limit current.
Reversed polarity normally prevents light output.
Never connect an LED directly across a power supply.

## Slide 35: LED Circuit Diagram
Positive supply -> resistor -> LED anode -> LED cathode -> negative supply
For a 5 V supply, a typical red LED may drop about 2 V. A 330 ohm resistor gives a safe current for introductory work.
This is an estimate. Real component values vary.

## Slide 36: Practical Brief: Measure Before Building
Aim: Use a DMM safely, verify the parts, build a protected LED circuit, and record evidence.
In pairs:
Person A sets the meter and makes the measurement.
Person B checks the meter terminals, mode and probe position.
Swap roles after each measurement.
Required evidence: a completed table, a labelled sketch and one safety control.

## Slide 37: Practical Equipment and Roles
Per pair:
protected low-voltage DC supply or battery pack;
digital multimeter and leads;
breadboard and jumper wires;
330 ohm resistor;
red LED; and
isolated switch lead if supplied.
Before starting, identify the tutor-approved supply voltage and maximum current limit.

## Slide 38: Practical Procedure: Inspect and Measure
Inspect the leads, breadboard, resistor and LED. Report damage; do not improvise a repair.
With power off, set the meter to resistance and measure the resistor.
Record the measured resistance in ohms or kilohms.
Set the meter to DC voltage and verify the supply voltage.
Turn power off again before placing any component on the breadboard.
Tutor checkpoint: both partners show the correct meter lead positions.

## Slide 39: Practical Procedure: Build and Check
Place the resistor and LED in series on separate breadboard rows.
Check LED polarity: anode toward the resistor and positive supply.
Ask your partner to trace the intended path aloud: positive -> resistor -> LED -> negative.
Ask the tutor for a visual check if unsure.
Energise the circuit for a short observation.
Record whether the LED lights and whether any component warms up.
If the LED does not light, turn power off before investigating.

## Slide 40: Practical Troubleshooting Ladder
If the LED does not light:
turn the power off;
check supply voltage with the meter;
check LED polarity;
check that each lead is in the intended breadboard row;
check the resistor value and placement;
check for a complete path from positive to negative; and
request tutor support before changing the circuit at random.
Good fault finding changes one thing at a time and records what was checked.

## Slide 41: Practical Recording Table
Item | Expected | Measured/observed | Unit or evidence
Supply voltage | tutor-stated value |  | V
Resistor | 330 ohm nominal |  | ohm or kilohm
LED orientation | anode to positive |  | sketch/check
LED result | lights without heating |  | observation
One safety control | power off before rewiring |  | statement

## Slide 42
Add a labelled circuit sketch showing the supply, resistor, LED and polarity.

## Slide 43: Mid-Practical Review
Pause and compare your work against these questions:
Can you point to the energy path in your LED circuit?
Why is the resistor included?
Where are voltage and resistance measured differently?
What must happen before moving a meter lead or rewiring a breadboard?
Resolve any unanswered question with your partner or tutor before continuing.

## Slide 44: Extension: From LED to Vehicle
Use the same system-thinking approach for a small vehicle.
LED circuit | Vehicle system
Supply | battery pack
Resistor protects LED current | fuse and driver protect motor circuit
LED produces visible output | motor produces motion
Switch can request action | sensor can request a behaviour

## Slide 45
The component choices differ, but safe power and clear information paths remain essential.

## Slide 46: Evidence Check: Annotate a System
Individually, draw a block diagram for a vehicle that:
uses a battery;
drives a motor and wheel;
stops when a limit switch is pressed; and
includes suitable protection.
Label:
the energy path;
the information path;
the controller; and
one safety component.
Time: 4 minutes.

## Slide 47: Exit Ticket
Complete these before leaving:
What is the difference between an energy path and an information path?
A 6 V load draws 0.20 A. Calculate its power.
State one reason an LED needs a resistor.
State one rule for safe multimeter use.
Name one component that must not be connected directly to a microcontroller output pin.
Hand in or photograph your annotated block diagram and measurement table as directed.

## Slide 48: Key Takeaways
Mechatronics combines mechanics, electrical energy, sensing, control and actuation.
Separate the energy path from the information path when thinking about a design.
Voltage, current, resistance and power have distinct meanings and units.
links voltage, current and power.
Measure before building, check polarity, and isolate power before rewiring.
A systematic check is safer and faster than trial-and-error wiring.

## Slide 49: Next Session
Week 2: DC Circuits and Digital Inputs
Next we will use:
Ohm’s law, ;
series and parallel circuits;
LED resistor selection; and
stable switch inputs using pull-up and pull-down resistors.
Bring this week’s block diagram and measurement record.