## Slide 1
UNIT 5009 / WEEK 07 / LO2
5 MIN
P4 / M2
Rebuild last week's connection
KEY IDEAS
Learners label one physical link, one protocol, one endpoint, and one data value from their Week 6 diagram.
IMAGE PLACEHOLDER
ADD PHOTO OR DIAGRAM
Leave this area open for the final visual
VISUAL BRIEF / Rebuild last week's connection
Full image-generation prompt is in this slide's speaker notes.
NETWORKED BUSES AND HMI/SCADA INTEGRATION
01 / 18
Notes: Networked Buses and HMI/SCADA Integration | Week 07 | LO2 Slide 1 of 18 | Suggested time: 5 minutes | Criteria: P4 / M2 TEACHING NOTES AND ACTIVITY CUES 1. Learners label one physical link, one protocol, one endpoint, and one data value from their Week 6 diagram. IMAGE PROMPT Create an original, technically plausible landscape visual for a vocational engineering presentation about Rebuild last week's connection. Show: Learners label one physical link, one protocol, one endpoint, and one data value from their Week 6 diagram.. Use an editorial technical-illustration style with accurate industrial components, a clean pale background, and restrained navy, teal, and muted amber accents. Compose the subject clearly for a right-side image panel. Do not include text, labels, numbers, logos, watermarks, or branded equipment. IMAGE PLACEMENT Replace the labelled image placeholder on the right with the generated or selected visual. Keep the title and key ideas unobstructed.

## Slide 2
UNIT 5009 / WEEK 07 / LO2
5 MIN
P4 / M2
Packaging line expansion scenario
KEY IDEAS
Add a second station and maintenance workstation to MedPack; ask how wiring, diagnosis, and data access change.
IMAGE PLACEHOLDER
ADD PHOTO OR DIAGRAM
Leave this area open for the final visual
VISUAL BRIEF / Packaging line expansion scenario
Full image-generation prompt is in this slide's speaker notes.
NETWORKED BUSES AND HMI/SCADA INTEGRATION
02 / 18
Notes: Networked Buses and HMI/SCADA Integration | Week 07 | LO2 Slide 2 of 18 | Suggested time: 5 minutes | Criteria: P4 / M2 TEACHING NOTES AND ACTIVITY CUES 1. Add a second station and maintenance workstation to MedPack; ask how wiring, diagnosis, and data access change. IMAGE PROMPT Create an original, technically plausible landscape visual for a vocational engineering presentation about Packaging line expansion scenario. Show: Add a second station and maintenance workstation to MedPack; ask how wiring, diagnosis, and data access change.. Use an editorial technical-illustration style with accurate industrial components, a clean pale background, and restrained navy, teal, and muted amber accents. Compose the subject clearly for a right-side image panel. Do not include text, labels, numbers, logos, watermarks, or branded equipment. IMAGE PLACEMENT Replace the labelled image placeholder on the right with the generated or selected visual. Keep the title and key ideas unobstructed.

## Slide 3
UNIT 5009 / WEEK 07 / LO2
5 MIN
P4 / M2
P4/M2 outcomes
KEY IDEAS
P4 requires a contextual review of bus advantages; M2 requires showing integration, not merely defining HMI and SCADA.
IMAGE PLACEHOLDER
ADD PHOTO OR DIAGRAM
Leave this area open for the final visual
VISUAL BRIEF / P4/M2 outcomes
Full image-generation prompt is in this slide's speaker notes.
NETWORKED BUSES AND HMI/SCADA INTEGRATION
03 / 18
Notes: Networked Buses and HMI/SCADA Integration | Week 07 | LO2 Slide 3 of 18 | Suggested time: 5 minutes | Criteria: P4 / M2 TEACHING NOTES AND ACTIVITY CUES 1. P4 requires a contextual review of bus advantages; M2 requires showing integration, not merely defining HMI and SCADA. IMAGE PROMPT Create an original, technically plausible landscape visual for a vocational engineering presentation about P4/M2 outcomes. Show: P4 requires a contextual review of bus advantages; M2 requires showing integration, not merely defining HMI and SCADA.. Use an editorial technical-illustration style with accurate industrial components, a clean pale background, and restrained navy, teal, and muted amber accents. Compose the subject clearly for a right-side image panel. Do not include text, labels, numbers, logos, watermarks, or branded equipment. IMAGE PLACEMENT Replace the labelled image placeholder on the right with the generated or selected visual. Keep the title and key ideas unobstructed.

## Slide 4
UNIT 5009 / WEEK 07 / LO2
12 MIN
P4 / M2
Point-to-point wiring versus networked I/O
KEY IDEAS
Compare central PLC wiring with remote I/O or bus-connected devices.
Identify PLC, network, remote-I/O coupler, device, power, and engineering diagnostics.
IMAGE PLACEHOLDER
ADD PHOTO OR DIAGRAM
Leave this area open for the final visual
VISUAL BRIEF / Point-to-point wiring versus networked I/O
Full image-generation prompt is in this slide's speaker notes.
NETWORKED BUSES AND HMI/SCADA INTEGRATION
04 / 18
Notes: Networked Buses and HMI/SCADA Integration | Week 07 | LO2 Slide 4 of 18 | Suggested time: 12 minutes | Criteria: P4 / M2 TEACHING NOTES AND ACTIVITY CUES 1. Compare central PLC wiring with remote I/O or bus-connected devices. 2. Identify PLC, network, remote-I/O coupler, device, power, and engineering diagnostics. IMAGE PROMPT Create an original, technically plausible landscape visual for a vocational engineering presentation about Point-to-point wiring versus networked I/O. Show: Compare central PLC wiring with remote I/O or bus-connected devices. Identify PLC, network, remote-I/O coupler, device, power, and engineering diagnostics.. Use an editorial technical-illustration style with accurate industrial components, a clean pale background, and restrained navy, teal, and muted amber accents. Compose the subject clearly for a right-side image panel. Do not include text, labels, numbers, logos, watermarks, or branded equipment. IMAGE PLACEMENT Replace the labelled image placeholder on the right with the generated or selected visual. Keep the title and key ideas unobstructed.

## Slide 5
UNIT 5009 / WEEK 07 / LO2
13 MIN
P4 / M2
Network topology and system boundaries
KEY IDEAS
Review line, star, ring, and bus arrangements and the role of switches, termination, addressing, and redundancy where supported.
Discuss cable distance, EMC, segmentation, power supply, and configuration management.
IMAGE PLACEHOLDER
ADD PHOTO OR DIAGRAM
Leave this area open for the final visual
VISUAL BRIEF / Network topology and system boundaries
Full image-generation prompt is in this slide's speaker notes.
NETWORKED BUSES AND HMI/SCADA INTEGRATION
05 / 18
Notes: Networked Buses and HMI/SCADA Integration | Week 07 | LO2 Slide 5 of 18 | Suggested time: 13 minutes | Criteria: P4 / M2 TEACHING NOTES AND ACTIVITY CUES 1. Review line, star, ring, and bus arrangements and the role of switches, termination, addressing, and redundancy where supported. 2. Discuss cable distance, EMC, segmentation, power supply, and configuration management. IMAGE PROMPT Create an original, technically plausible landscape visual for a vocational engineering presentation about Network topology and system boundaries. Show: Review line, star, ring, and bus arrangements and the role of switches, termination, addressing, and redundancy where supported. Discuss cable distance, EMC, segmentation, power supply, and configuration management.. Use an editorial technical-illustration style with accurate industrial components, a clean pale background, and restrained navy, teal, and muted amber accents. Compose the subject clearly for a right-side image panel. Do not include text, labels, numbers, logos, watermarks, or branded equipment. IMAGE PLACEMENT Replace the labelled image placeholder on the right with the generated or selected visual. Keep the title and key ideas unobstructed.

## Slide 6
UNIT 5009 / WEEK 07 / LO2
12 MIN
P4 / M2
Distributed I/O architecture
KEY IDEAS
Explain how remote I/O places channels nearer field devices and sends data to the PLC over a supported network.
Consider update time, module diagnostics, channel configuration, node loss, and local/remote fault isolation.
IMAGE PLACEHOLDER
ADD PHOTO OR DIAGRAM
Leave this area open for the final visual
VISUAL BRIEF / Distributed I/O architecture
Full image-generation prompt is in this slide's speaker notes.
NETWORKED BUSES AND HMI/SCADA INTEGRATION
06 / 18
Notes: Networked Buses and HMI/SCADA Integration | Week 07 | LO2 Slide 6 of 18 | Suggested time: 12 minutes | Criteria: P4 / M2 TEACHING NOTES AND ACTIVITY CUES 1. Explain how remote I/O places channels nearer field devices and sends data to the PLC over a supported network. 2. Consider update time, module diagnostics, channel configuration, node loss, and local/remote fault isolation. IMAGE PROMPT Create an original, technically plausible landscape visual for a vocational engineering presentation about Distributed I/O architecture. Show: Explain how remote I/O places channels nearer field devices and sends data to the PLC over a supported network. Consider update time, module diagnostics, channel configuration, node loss, and local/remote fault isolation.. Use an editorial technical-illustration style with accurate industrial components, a clean pale background, and restrained navy, teal, and muted amber accents. Compose the subject clearly for a right-side image panel. Do not include text, labels, numbers, logos, watermarks, or branded equipment. IMAGE PLACEMENT Replace the labelled image placeholder on the right with the generated or selected visual. Keep the title and key ideas unobstructed.

## Slide 7
UNIT 5009 / WEEK 07 / LO2
13 MIN
P4 / M2
Draw a MedPack bus architecture
KEY IDEAS
Teams map PLC, local I/O, remote I/O, pill sensor, actuator interface, HMI, SCADA workstation, and engineering access.
Label each link and protocol; show the safety boundary and identify local control dependencies.
IMAGE PLACEHOLDER
ADD PHOTO OR DIAGRAM
Leave this area open for the final visual
VISUAL BRIEF / Draw a MedPack bus architecture
Full image-generation prompt is in this slide's speaker notes.
NETWORKED BUSES AND HMI/SCADA INTEGRATION
07 / 18
Notes: Networked Buses and HMI/SCADA Integration | Week 07 | LO2 Slide 7 of 18 | Suggested time: 13 minutes | Criteria: P4 / M2 TEACHING NOTES AND ACTIVITY CUES 1. Teams map PLC, local I/O, remote I/O, pill sensor, actuator interface, HMI, SCADA workstation, and engineering access. 2. Label each link and protocol; show the safety boundary and identify local control dependencies. IMAGE PROMPT Create an original, technically plausible landscape visual for a vocational engineering presentation about Draw a MedPack bus architecture. Show: Teams map PLC, local I/O, remote I/O, pill sensor, actuator interface, HMI, SCADA workstation, and engineering access. Label each link and protocol; show the safety boundary and identify local control dependencies.. Use an editorial technical-illustration style with accurate industrial components, a clean pale background, and restrained navy, teal, and muted amber accents. Compose the subject clearly for a right-side image panel. Do not include text, labels, numbers, logos, watermarks, or branded equipment. IMAGE PLACEMENT Replace the labelled image placeholder on the right with the generated or selected visual. Keep the title and key ideas unobstructed.

## Slide 8
UNIT 5009 / WEEK 07 / LO2
10 MIN
P4 / M2
Review bus-system advantages
KEY IDEAS
Explain reduced point-to-point wiring, easier expansion, modularity, distributed I/O, device diagnostics, maintenance visibility, and data availability.
Tie every advantage to line installation, downtime, or maintenance in the scenario.
IMAGE PLACEHOLDER
ADD PHOTO OR DIAGRAM
Leave this area open for the final visual
VISUAL BRIEF / Review bus-system advantages
Full image-generation prompt is in this slide's speaker notes.
NETWORKED BUSES AND HMI/SCADA INTEGRATION
08 / 18
Notes: Networked Buses and HMI/SCADA Integration | Week 07 | LO2 Slide 8 of 18 | Suggested time: 10 minutes | Criteria: P4 / M2 TEACHING NOTES AND ACTIVITY CUES 1. Explain reduced point-to-point wiring, easier expansion, modularity, distributed I/O, device diagnostics, maintenance visibility, and data availability. 2. Tie every advantage to line installation, downtime, or maintenance in the scenario. IMAGE PROMPT Create an original, technically plausible landscape visual for a vocational engineering presentation about Review bus-system advantages. Show: Explain reduced point-to-point wiring, easier expansion, modularity, distributed I/O, device diagnostics, maintenance visibility, and data availability. Tie every advantage to line installation, downtime, or maintenance in the scenario.. Use an editorial technical-illustration style with accurate industrial components, a clean pale background, and restrained navy, teal, and muted amber accents. Compose the subject clearly for a right-side image panel. Do not include text, labels, numbers, logos, watermarks, or branded equipment. IMAGE PLACEMENT Replace the labelled image placeholder on the right with the generated or selected visual. Keep the title and key ideas unobstructed.

## Slide 9
UNIT 5009 / WEEK 07 / LO2
15 MIN
P4 / M2
Review constraints and failure modes
KEY IDEAS
Evaluate network hardware cost, configuration skill, interoperability, vendor dependence, cyber exposure, shared failure domains, latency/update limits, and recovery planning.
Ask when a hardwired design may remain preferable.
IMAGE PLACEHOLDER
ADD PHOTO OR DIAGRAM
Leave this area open for the final visual
VISUAL BRIEF / Review constraints and failure modes
Full image-generation prompt is in this slide's speaker notes.
NETWORKED BUSES AND HMI/SCADA INTEGRATION
09 / 18
Notes: Networked Buses and HMI/SCADA Integration | Week 07 | LO2 Slide 9 of 18 | Suggested time: 15 minutes | Criteria: P4 / M2 TEACHING NOTES AND ACTIVITY CUES 1. Evaluate network hardware cost, configuration skill, interoperability, vendor dependence, cyber exposure, shared failure domains, latency/update limits, and recovery planning. 2. Ask when a hardwired design may remain preferable. IMAGE PROMPT Create an original, technically plausible landscape visual for a vocational engineering presentation about Review constraints and failure modes. Show: Evaluate network hardware cost, configuration skill, interoperability, vendor dependence, cyber exposure, shared failure domains, latency/update limits, and recovery planning. Ask when a hardwired design may remain preferable.. Use an editorial technical-illustration style with accurate industrial components, a clean pale background, and restrained navy, teal, and muted amber accents. Compose the subject clearly for a right-side image panel. Do not include text, labels, numbers, logos, watermarks, or branded equipment. IMAGE PLACEMENT Replace the labelled image placeholder on the right with the generated or selected visual. Keep the title and key ideas unobstructed.

## Slide 10
UNIT 5009 / WEEK 07 / LO2
10 MIN
P4 / M2
P4 claim-evidence-consequence activity
KEY IDEAS
Teams make two claims about bus-system value and support each with a MedPack consequence and a counterpoint.
Reject generic claims such as "less wiring is always cheaper" unless installed cost is demonstrated.
IMAGE PLACEHOLDER
ADD PHOTO OR DIAGRAM
Leave this area open for the final visual
VISUAL BRIEF / P4 claim-evidence-consequence activity
Full image-generation prompt is in this slide's speaker notes.
NETWORKED BUSES AND HMI/SCADA INTEGRATION
10 / 18
Notes: Networked Buses and HMI/SCADA Integration | Week 07 | LO2 Slide 10 of 18 | Suggested time: 10 minutes | Criteria: P4 / M2 TEACHING NOTES AND ACTIVITY CUES 1. Teams make two claims about bus-system value and support each with a MedPack consequence and a counterpoint. 2. Reject generic claims such as "less wiring is always cheaper" unless installed cost is demonstrated. IMAGE PROMPT Create an original, technically plausible landscape visual for a vocational engineering presentation about P4 claim-evidence-consequence activity. Show: Teams make two claims about bus-system value and support each with a MedPack consequence and a counterpoint. Reject generic claims such as "less wiring is always cheaper" unless installed cost is demonstrated.. Use an editorial technical-illustration style with accurate industrial components, a clean pale background, and restrained navy, teal, and muted amber accents. Compose the subject clearly for a right-side image panel. Do not include text, labels, numbers, logos, watermarks, or branded equipment. IMAGE PLACEMENT Replace the labelled image placeholder on the right with the generated or selected visual. Keep the title and key ideas unobstructed.

## Slide 11
UNIT 5009 / WEEK 07 / LO2
10 MIN
P4 / M2
HMI and SCADA roles
KEY IDEAS
HMI: local operator status, commands, alarms, and process navigation.
SCADA: supervisory acquisition, alarm/event management, trends, historian, and multiple assets; products can combine roles.
Explain that role and system scale matter more than product label.
IMAGE PLACEHOLDER
ADD PHOTO OR DIAGRAM
Leave this area open for the final visual
VISUAL BRIEF / HMI and SCADA roles
Full image-generation prompt is in this slide's speaker notes.
NETWORKED BUSES AND HMI/SCADA INTEGRATION
11 / 18
Notes: Networked Buses and HMI/SCADA Integration | Week 07 | LO2 Slide 11 of 18 | Suggested time: 10 minutes | Criteria: P4 / M2 TEACHING NOTES AND ACTIVITY CUES 1. HMI: local operator status, commands, alarms, and process navigation. 2. SCADA: supervisory acquisition, alarm/event management, trends, historian, and multiple assets; products can combine roles. 3. Explain that role and system scale matter more than product label. IMAGE PROMPT Create an original, technically plausible landscape visual for a vocational engineering presentation about HMI and SCADA roles. Show: HMI: local operator status, commands, alarms, and process navigation. SCADA: supervisory acquisition, alarm/event management, trends, historian, and multiple assets; products can combine roles.. Use an editorial technical-illustration style with accurate industrial components, a clean pale background, and restrained navy, teal, and muted amber accents. Compose the subject clearly for a right-side image panel. Do not include text, labels, numbers, logos, watermarks, or branded equipment. IMAGE PLACEMENT Replace the labelled image placeholder on the right with the generated or selected visual. Keep the title and key ideas unobstructed.

## Slide 12
UNIT 5009 / WEEK 07 / LO2
15 MIN
P4 / M2
PLC-HMI-SCADA architecture
KEY IDEAS
Draw field devices -> PLC local control -> industrial network -> HMI/SCADA services/client -> history/reporting.
Mark protocols, data direction, network boundaries, ownership of logic, and failure behaviour.
Keep essential sequencing and safety functions independent of supervisory availability.
IMAGE PLACEHOLDER
ADD PHOTO OR DIAGRAM
Leave this area open for the final visual
VISUAL BRIEF / PLC-HMI-SCADA architecture
Full image-generation prompt is in this slide's speaker notes.
NETWORKED BUSES AND HMI/SCADA INTEGRATION
12 / 18
Notes: Networked Buses and HMI/SCADA Integration | Week 07 | LO2 Slide 12 of 18 | Suggested time: 15 minutes | Criteria: P4 / M2 TEACHING NOTES AND ACTIVITY CUES 1. Draw field devices -> PLC local control -> industrial network -> HMI/SCADA services/client -> history/reporting. 2. Mark protocols, data direction, network boundaries, ownership of logic, and failure behaviour. 3. Keep essential sequencing and safety functions independent of supervisory availability. IMAGE PROMPT Create an original, technically plausible landscape visual for a vocational engineering presentation about PLC-HMI-SCADA architecture. Show: Draw field devices -> PLC local control -> industrial network -> HMI/SCADA services/client -> history/reporting. Mark protocols, data direction, network boundaries, ownership of logic, and failure behaviour.. Use an editorial technical-illustration style with accurate industrial components, a clean pale background, and restrained navy, teal, and muted amber accents. Compose the subject clearly for a right-side image panel. Do not include text, labels, numbers, logos, watermarks, or branded equipment. IMAGE PLACEMENT Replace the labelled image placeholder on the right with the generated or selected visual. Keep the title and key ideas unobstructed.

## Slide 13
UNIT 5009 / WEEK 07 / LO2
10 MIN
P4 / M2
MedPack tag list and access rights
KEY IDEAS
Read-only examples: RunState, PillCount, TargetCount, FaultCode, ActuatorStatus, EStopStatusReadOnly.
Requested commands: StartRequest and ResetRequest; PLC validates permissives and process state.
Include tag type, units, address/name, update rate, alarm/quality handling, and read/write permission.
IMAGE PLACEHOLDER
ADD PHOTO OR DIAGRAM
Leave this area open for the final visual
VISUAL BRIEF / MedPack tag list and access rights
Full image-generation prompt is in this slide's speaker notes.
NETWORKED BUSES AND HMI/SCADA INTEGRATION
13 / 18
Notes: Networked Buses and HMI/SCADA Integration | Week 07 | LO2 Slide 13 of 18 | Suggested time: 10 minutes | Criteria: P4 / M2 TEACHING NOTES AND ACTIVITY CUES 1. Read-only examples: RunState, PillCount, TargetCount, FaultCode, ActuatorStatus, EStopStatusReadOnly. 2. Requested commands: StartRequest and ResetRequest; PLC validates permissives and process state. 3. Include tag type, units, address/name, update rate, alarm/quality handling, and read/write permission. IMAGE PROMPT Create an original, technically plausible landscape visual for a vocational engineering presentation about MedPack tag list and access rights. Show: Read-only examples: RunState, PillCount, TargetCount, FaultCode, ActuatorStatus, EStopStatusReadOnly. Requested commands: StartRequest and ResetRequest; PLC validates permissives and process state.. Use an editorial technical-illustration style with accurate industrial components, a clean pale background, and restrained navy, teal, and muted amber accents. Compose the subject clearly for a right-side image panel. Do not include text, labels, numbers, logos, watermarks, or branded equipment. IMAGE PLACEMENT Replace the labelled image placeholder on the right with the generated or selected visual. Keep the title and key ideas unobstructed.

## Slide 14
UNIT 5009 / WEEK 07 / LO2
10 MIN
P4 / M2
Data-quality and operator-display rules
KEY IDEAS
Explain stale/unknown quality, scaling, address offsets, data type, units, alarm acknowledgement, and clear status indication.
Dashboard must distinguish disconnected/stale data from a valid zero.
Avoid using an HMI control as an E-stop or safety reset path.
IMAGE PLACEHOLDER
ADD PHOTO OR DIAGRAM
Leave this area open for the final visual
VISUAL BRIEF / Data-quality and operator-display rules
Full image-generation prompt is in this slide's speaker notes.
NETWORKED BUSES AND HMI/SCADA INTEGRATION
14 / 18
Notes: Networked Buses and HMI/SCADA Integration | Week 07 | LO2 Slide 14 of 18 | Suggested time: 10 minutes | Criteria: P4 / M2 TEACHING NOTES AND ACTIVITY CUES 1. Explain stale/unknown quality, scaling, address offsets, data type, units, alarm acknowledgement, and clear status indication. 2. Dashboard must distinguish disconnected/stale data from a valid zero. 3. Avoid using an HMI control as an E-stop or safety reset path. IMAGE PROMPT Create an original, technically plausible landscape visual for a vocational engineering presentation about Data-quality and operator-display rules. Show: Explain stale/unknown quality, scaling, address offsets, data type, units, alarm acknowledgement, and clear status indication. Dashboard must distinguish disconnected/stale data from a valid zero.. Use an editorial technical-illustration style with accurate industrial components, a clean pale background, and restrained navy, teal, and muted amber accents. Compose the subject clearly for a right-side image panel. Do not include text, labels, numbers, logos, watermarks, or branded equipment. IMAGE PLACEMENT Replace the labelled image placeholder on the right with the generated or selected visual. Keep the title and key ideas unobstructed.

## Slide 15
UNIT 5009 / WEEK 07 / LO2
20 MIN
P4 / M2
PLC-to-dashboard demonstration
KEY IDEAS
If available, use Node-RED/Modbus TCP or the actual supported protocol to read a verified PLC tag and display state/count.
Demonstrate endpoint, protocol, address, data type, scaling, polling/update, and bad-connection indication.
If hardware is unavailable, use a fully labelled architecture, tag mapping, and example data flow.
The local guide's example addresses are illustrative; verify the live PLC map and zero/one-based convention.
IMAGE PLACEHOLDER
ADD PHOTO OR DIAGRAM
Leave this area open for the final visual
VISUAL BRIEF / PLC-to-dashboard demonstration
Full image-generation prompt is in this slide's speaker notes.
NETWORKED BUSES AND HMI/SCADA INTEGRATION
15 / 18
Notes: Networked Buses and HMI/SCADA Integration | Week 07 | LO2 Slide 15 of 18 | Suggested time: 20 minutes | Criteria: P4 / M2 TEACHING NOTES AND ACTIVITY CUES 1. If available, use Node-RED/Modbus TCP or the actual supported protocol to read a verified PLC tag and display state/count. 2. Demonstrate endpoint, protocol, address, data type, scaling, polling/update, and bad-connection indication. 3. If hardware is unavailable, use a fully labelled architecture, tag mapping, and example data flow. 4. The local guide's example addresses are illustrative; verify the live PLC map and zero/one-based convention. IMAGE PROMPT Create an original, technically plausible landscape visual for a vocational engineering presentation about PLC-to-dashboard demonstration. Show: If available, use Node-RED/Modbus TCP or the actual supported protocol to read a verified PLC tag and display state/count. Demonstrate endpoint, protocol, address, data type, scaling, polling/update, and bad-connection indication.. Use an editorial technical-illustration style with accurate industrial components, a clean pale background, and restrained navy, teal, and muted amber accents. Compose the subject clearly for a right-side image panel. Do not include text, labels, numbers, logos, watermarks, or branded equipment. IMAGE PLACEMENT Replace the labelled image placeholder on the right with the generated or selected visual. Keep the title and key ideas unobstructed.

## Slide 16
UNIT 5009 / WEEK 07 / LO2
20 MIN
P4 / M2
M2 integration design challenge
KEY IDEAS
Teams produce architecture plus tag table and explain one read value and one requested command end-to-end.
Peer asks where the PLC validates the command, what the screen shows during connection loss, and what evidence proves the mapping.
IMAGE PLACEHOLDER
ADD PHOTO OR DIAGRAM
Leave this area open for the final visual
VISUAL BRIEF / M2 integration design challenge
Full image-generation prompt is in this slide's speaker notes.
NETWORKED BUSES AND HMI/SCADA INTEGRATION
16 / 18
Notes: Networked Buses and HMI/SCADA Integration | Week 07 | LO2 Slide 16 of 18 | Suggested time: 20 minutes | Criteria: P4 / M2 TEACHING NOTES AND ACTIVITY CUES 1. Teams produce architecture plus tag table and explain one read value and one requested command end-to-end. 2. Peer asks where the PLC validates the command, what the screen shows during connection loss, and what evidence proves the mapping. IMAGE PROMPT Create an original, technically plausible landscape visual for a vocational engineering presentation about M2 integration design challenge. Show: Teams produce architecture plus tag table and explain one read value and one requested command end-to-end. Peer asks where the PLC validates the command, what the screen shows during connection loss, and what evidence proves the mapping.. Use an editorial technical-illustration style with accurate industrial components, a clean pale background, and restrained navy, teal, and muted amber accents. Compose the subject clearly for a right-side image panel. Do not include text, labels, numbers, logos, watermarks, or branded equipment. IMAGE PLACEMENT Replace the labelled image placeholder on the right with the generated or selected visual. Keep the title and key ideas unobstructed.

## Slide 17
UNIT 5009 / WEEK 07 / LO2
7 MIN
P4 / M2
Criteria evidence review
KEY IDEAS
P4: explain reduced wiring, expansion, diagnostics, modularity/distributed I/O, and monitoring data with station-specific consequences and trade-offs.
M2: show protocol, architecture, named tags, and data flow through working evidence or clear equivalent documentation.
IMAGE PLACEHOLDER
ADD PHOTO OR DIAGRAM
Leave this area open for the final visual
VISUAL BRIEF / Criteria evidence review
Full image-generation prompt is in this slide's speaker notes.
NETWORKED BUSES AND HMI/SCADA INTEGRATION
17 / 18
Notes: Networked Buses and HMI/SCADA Integration | Week 07 | LO2 Slide 17 of 18 | Suggested time: 7 minutes | Criteria: P4 / M2 TEACHING NOTES AND ACTIVITY CUES 1. P4: explain reduced wiring, expansion, diagnostics, modularity/distributed I/O, and monitoring data with station-specific consequences and trade-offs. 2. M2: show protocol, architecture, named tags, and data flow through working evidence or clear equivalent documentation. IMAGE PROMPT Create an original, technically plausible landscape visual for a vocational engineering presentation about Criteria evidence review. Show: P4: explain reduced wiring, expansion, diagnostics, modularity/distributed I/O, and monitoring data with station-specific consequences and trade-offs. M2: show protocol, architecture, named tags, and data flow through working evidence or clear equivalent documentation.. Use an editorial technical-illustration style with accurate industrial components, a clean pale background, and restrained navy, teal, and muted amber accents. Compose the subject clearly for a right-side image panel. Do not include text, labels, numbers, logos, watermarks, or branded equipment. IMAGE PLACEMENT Replace the labelled image placeholder on the right with the generated or selected visual. Keep the title and key ideas unobstructed.

## Slide 18
UNIT 5009 / WEEK 07 / LO2
8 MIN
P4 / M2
Exit ticket: one bus benefit, one integration proof
KEY IDEAS
State one justified bus advantage and one limitation; name the artifact that proves PLC-HMI/SCADA integration.
IMAGE PLACEHOLDER
ADD PHOTO OR DIAGRAM
Leave this area open for the final visual
VISUAL BRIEF / Exit ticket: one bus benefit, one integration proof
Full image-generation prompt is in this slide's speaker notes.
NETWORKED BUSES AND HMI/SCADA INTEGRATION
18 / 18
Notes: Networked Buses and HMI/SCADA Integration | Week 07 | LO2 Slide 18 of 18 | Suggested time: 8 minutes | Criteria: P4 / M2 TEACHING NOTES AND ACTIVITY CUES 1. State one justified bus advantage and one limitation; name the artifact that proves PLC-HMI/SCADA integration. IMAGE PROMPT Create an original, technically plausible landscape visual for a vocational engineering presentation about Exit ticket: one bus benefit, one integration proof. Show: State one justified bus advantage and one limitation; name the artifact that proves PLC-HMI/SCADA integration.. Use an editorial technical-illustration style with accurate industrial components, a clean pale background, and restrained navy, teal, and muted amber accents. Compose the subject clearly for a right-side image panel. Do not include text, labels, numbers, logos, watermarks, or branded equipment. IMAGE PLACEMENT Replace the labelled image placeholder on the right with the generated or selected visual. Keep the title and key ideas unobstructed.