## Slide 1
UNIT 5009 / WEEK 05 / LO2
5 MIN
LO2 FOUNDATIONS
A false count can stop a production line
TEACHING POINTS
01
A sensor pulse is the electrical representation of one detected pill; contact bounce or electrical noise can create extra transitions, while a pulse shorter than the input can register may be missed.
02
Have learners follow a trace containing one clean event and one bouncing event; the expected count depends on the configured input filter, edge logic, and capture method, not on the drawing alone.
03
In a clearly hypothetical case, a missed count leaves PillCount below target, so the PLC should not assert the target-reached request; verify the actual sequence and permissives in the project.
SUGGESTED VISUAL
IMAGE SPACE
Insert the visual described in the speaker notes
SIGNAL PROCESSING AND SIGNAL INTEGRITY
01 / 18
Notes: Signal Processing and Signal Integrity | Week 05 | LO2 Slide 1 of 18 | Suggested time: 5 minutes | Criteria: LO2 foundations TEACHING NOTES AND ACTIVITY CUES 1. A sensor pulse is the electrical representation of one detected pill; contact bounce or electrical noise can create extra transitions, while a pulse shorter than the input can register may be missed. 2. Have learners follow a trace containing one clean event and one bouncing event; the expected count depends on the configured input filter, edge logic, and capture method, not on the drawing alone. 3. In a clearly hypothetical case, a missed count leaves PillCount below target, so the PLC should not assert the target-reached request; verify the actual sequence and permissives in the project. TEACHING VISUAL This slide has a reserved image bay. Add the image described below. OPTIONAL IMAGE PROMPT Original oscilloscope-style timing diagram showing a sensor voltage with one clean pulse, one bouncing pulse, and a PLC input-state trace below it; no labels or embedded text.

## Slide 2
UNIT 5009 / WEEK 05 / LO2
5 MIN
LO2 FOUNDATIONS
Reconnect LO1 to LO2
TEACHING POINTS
01
Reopen the selected PLC CPU/module, sensor datasheet, I/O schedule, and load assumptions from Weeks 1-4; use those actual choices rather than inventing terminal addresses or voltage ratings.
02
Trace the pill sensor from its specified output type and supply through the assigned input channel to the program tag used by the count logic.
03
Check the design fit: the sensor's electrical output, module input type, filter capability, and expected event rate must all be compatible; a correct program cannot repair a mismatched electrical interface.
APPLICATION WORKFLOW
Application need
PLC feature
System impact
Evidence
Trace the requirement from the device to its verified result
SIGNAL PROCESSING AND SIGNAL INTEGRITY
02 / 18
Notes: Signal Processing and Signal Integrity | Week 05 | LO2 Slide 2 of 18 | Suggested time: 5 minutes | Criteria: LO2 foundations TEACHING NOTES AND ACTIVITY CUES 1. Reopen the selected PLC CPU/module, sensor datasheet, I/O schedule, and load assumptions from Weeks 1-4; use those actual choices rather than inventing terminal addresses or voltage ratings. 2. Trace the pill sensor from its specified output type and supply through the assigned input channel to the program tag used by the count logic. 3. Check the design fit: the sensor's electrical output, module input type, filter capability, and expected event rate must all be compatible; a correct program cannot repair a mismatched electrical interface. TEACHING VISUAL The slide uses an editable application workflow diagram. Keep it unless the prompted image communicates the idea more clearly. OPTIONAL IMAGE PROMPT Original engineering desk scene with a PLC module, sensor datasheet, wiring plan, and highlighted signal path connected by a pencil line; no readable text or logos.

## Slide 3
UNIT 5009 / WEEK 05 / LO2
5 MIN
LO2 FOUNDATIONS
Session outcomes and evidence
TEACHING POINTS
01
By the end, learners should trace a field signal to a program value and output, explain scan/filter/edge effects, and select a suitable method for capturing fast events.
02
Practical evidence is a normal-cycle check plus a controlled fault test with conditions, expected result, observed result, diagnosis, correction, and retest recorded.
03
This session supports LO2 wiring, operation, fault-finding, and signal-integrity evidence; Week 6 separately develops the P3 communication-link/protocol comparison.
FORMATIVE CHECK
01
EXPECTED STATE
02
MEASURE SIGNAL
03
FIND BOUNDARY
04
RETEST + RECORD
SIGNAL PROCESSING AND SIGNAL INTEGRITY
03 / 18
Notes: Signal Processing and Signal Integrity | Week 05 | LO2 Slide 3 of 18 | Suggested time: 5 minutes | Criteria: LO2 foundations TEACHING NOTES AND ACTIVITY CUES 1. By the end, learners should trace a field signal to a program value and output, explain scan/filter/edge effects, and select a suitable method for capturing fast events. 2. Practical evidence is a normal-cycle check plus a controlled fault test with conditions, expected result, observed result, diagnosis, correction, and retest recorded. 3. This session supports LO2 wiring, operation, fault-finding, and signal-integrity evidence; Week 6 separately develops the P3 communication-link/protocol comparison. TEACHING VISUAL The slide uses an editable formative check diagram. Keep it unless the prompted image communicates the idea more clearly. OPTIONAL IMAGE PROMPT Clean original flow diagram linking sensor, PLC input, program state, PLC output, actuator, and a lab-record sheet with arrows but no text.

## Slide 4
UNIT 5009 / WEEK 05 / LO2
12 MIN
LO2 FOUNDATIONS
From physical event to PLC variable
TEACHING POINTS
01
Follow one MedPack pill event through target detection, sensor electrical output, cable and terminal, input channel, PLC task/process data, count logic, output channel, and actuator interface.
02
Distinguish physical state from interpreted state: a sensor LED, module input LED, program tag, and output LED are separate observation points and may disagree when a fault lies between them.
03
At each boundary verify the device/module documentation for signal type, rated range, common/reference, isolation, filter, and diagnostic behaviour; do not assume every input is 24 V DC.
SIGNAL PATH
SENSOR +
BUTTONS
PLC
INPUTS
CPU
LOGIC
OUTPUT
INTERFACE
ACTUATOR / BUZZER
Verify voltage, polarity, load current and channel limits
SIGNAL PROCESSING AND SIGNAL INTEGRITY
04 / 18
Notes: Signal Processing and Signal Integrity | Week 05 | LO2 Slide 4 of 18 | Suggested time: 12 minutes | Criteria: LO2 foundations TEACHING NOTES AND ACTIVITY CUES 1. Follow one MedPack pill event through target detection, sensor electrical output, cable and terminal, input channel, PLC task/process data, count logic, output channel, and actuator interface. 2. Distinguish physical state from interpreted state: a sensor LED, module input LED, program tag, and output LED are separate observation points and may disagree when a fault lies between them. 3. At each boundary verify the device/module documentation for signal type, rated range, common/reference, isolation, filter, and diagnostic behaviour; do not assume every input is 24 V DC. TEACHING VISUAL The slide uses an editable signal path diagram. Keep it unless the prompted image communicates the idea more clearly. OPTIONAL IMAGE PROMPT Original cutaway-style signal-chain diagram showing a photoelectric sensor, terminal block, isolated PLC input circuit, program memory, output module, and relay interface; no labels or text.

## Slide 5
UNIT 5009 / WEEK 05 / LO2
13 MIN
LO2 FOUNDATIONS
Typical scan and response timeline
TEACHING POINTS
01
In a basic cyclic model, inputs are sampled, user logic executes, and outputs are updated; communications, task scheduling, and monitoring may run on separate or overlapping schedules.
02
Real controllers may use periodic tasks, interrupts, remote-I/O update cycles, or immediate I/O instructions, so use the selected CPU and module manuals to interpret the timing diagram.
03
In a hypothetical timing exercise, compare a 6 ms sensor pulse with a 10 ms task period and an input filter configured longer than the pulse; learners should predict a possible missed event, then identify what hardware documentation and test would settle it.
SIGNAL TIMING
RAW SENSOR: VALID EVENTS + CHATTER
QUALIFIED INPUT / ONE-SHOT EVENTS
Reject the short chatter; preserve all valid pill events
SIGNAL PROCESSING AND SIGNAL INTEGRITY
05 / 18
Notes: Signal Processing and Signal Integrity | Week 05 | LO2 Slide 5 of 18 | Suggested time: 13 minutes | Criteria: LO2 foundations TEACHING NOTES AND ACTIVITY CUES 1. In a basic cyclic model, inputs are sampled, user logic executes, and outputs are updated; communications, task scheduling, and monitoring may run on separate or overlapping schedules. 2. Real controllers may use periodic tasks, interrupts, remote-I/O update cycles, or immediate I/O instructions, so use the selected CPU and module manuals to interpret the timing diagram. 3. In a hypothetical timing exercise, compare a 6 ms sensor pulse with a 10 ms task period and an input filter configured longer than the pulse; learners should predict a possible missed event, then identify what hardware documentation and test would settle it. TEACHING VISUAL The slide uses an editable signal timing diagram. Keep it unless the prompted image communicates the idea more clearly. OPTIONAL IMAGE PROMPT Original layered timing diagram with sensor pulse, input sampling instants, PLC task execution blocks, output update, and network refresh shown on aligned timelines; no text.

## Slide 6
UNIT 5009 / WEEK 05 / LO2
12 MIN
LO2 FOUNDATIONS
Debounce and edge detection
TEACHING POINTS
01
An input filter rejects or delays short transitions at the hardware/channel level; rising-edge logic detects a false-to-true transition in the program. They address related but different causes.
02
A held-high sensor represents one transition, not repeated pills; a one-shot should count once until the input returns low, while bouncing can create multiple edges if not conditioned.
03
Set filter time only after checking the sensor's minimum pulse width and maximum event rate; a filter that is too long can suppress valid MedPack events.
04
Test procedure: apply one clean pulse, a held-high input, and a bouncing trace in simulation; expected observation is one count for one valid rising edge, with bounce behaviour matching the configured filter and logic.
SIGNAL TIMING
RAW SENSOR: VALID EVENTS + CHATTER
QUALIFIED INPUT / ONE-SHOT EVENTS
Reject the short chatter; preserve all valid pill events
SIGNAL PROCESSING AND SIGNAL INTEGRITY
06 / 18
Notes: Signal Processing and Signal Integrity | Week 05 | LO2 Slide 6 of 18 | Suggested time: 12 minutes | Criteria: LO2 foundations TEACHING NOTES AND ACTIVITY CUES 1. An input filter rejects or delays short transitions at the hardware/channel level; rising-edge logic detects a false-to-true transition in the program. They address related but different causes. 2. A held-high sensor represents one transition, not repeated pills; a one-shot should count once until the input returns low, while bouncing can create multiple edges if not conditioned. 3. Set filter time only after checking the sensor's minimum pulse width and maximum event rate; a filter that is too long can suppress valid MedPack events. 4. Test procedure: apply one clean pulse, a held-high input, and a bouncing trace in simulation; expected observation is one count for one valid rising edge, with bounce behaviour matching the configured filter and logic. TEACHING VISUAL The slide uses an editable signal timing diagram. Keep it unless the prompted image communicates the idea more clearly. OPTIONAL IMAGE PROMPT Original paired timing traces comparing contact bounce before filtering, a debounced input, and a one-shot count pulse; no labels or text.

## Slide 7
UNIT 5009 / WEEK 05 / LO2
13 MIN
LO2 FOUNDATIONS
High-speed pulse capture and count integrity
TEACHING POINTS
01
High-speed counter or capture functions can register events independently of ordinary cyclic logic, but only on supported channels and within documented frequency, pulse-width, voltage, and filter limits.
02
Clearly hypothetical example: at 40 events/s, consecutive events are 25 ms apart; a standard 10 ms task may observe transitions depending on phase and input update behaviour, so this arithmetic alone does not prove reliable capture.
03
Check the actual PLC/module manual for maximum count rate, minimum on/off time, filter setting, and buffer/overflow behaviour; use the specified high-speed input when ordinary sampling cannot be shown to meet requirements.
04
Verification procedure: generate a known pulse train below the documented limit, compare source and PLC totals over a fixed test interval, then repeat at the intended operating rate and inspect overflow/diagnostic status.
SIGNAL TIMING
RAW SENSOR: VALID EVENTS + CHATTER
QUALIFIED INPUT / ONE-SHOT EVENTS
Reject the short chatter; preserve all valid pill events
SIGNAL PROCESSING AND SIGNAL INTEGRITY
07 / 18
Notes: Signal Processing and Signal Integrity | Week 05 | LO2 Slide 7 of 18 | Suggested time: 13 minutes | Criteria: LO2 foundations TEACHING NOTES AND ACTIVITY CUES 1. High-speed counter or capture functions can register events independently of ordinary cyclic logic, but only on supported channels and within documented frequency, pulse-width, voltage, and filter limits. 2. Clearly hypothetical example: at 40 events/s, consecutive events are 25 ms apart; a standard 10 ms task may observe transitions depending on phase and input update behaviour, so this arithmetic alone does not prove reliable capture. 3. Check the actual PLC/module manual for maximum count rate, minimum on/off time, filter setting, and buffer/overflow behaviour; use the specified high-speed input when ordinary sampling cannot be shown to meet requirements. 4. Verification procedure: generate a known pulse train below the documented limit, compare source and PLC totals over a fixed test interval, then repeat at the intended operating rate and inspect overflow/diagnostic status. TEACHING VISUAL The slide uses an editable signal timing diagram. Keep it unless the prompted image communicates the idea more clearly. OPTIONAL IMAGE PROMPT Original PLC high-speed counter block connected to a pulse generator and sensor, with a stable count trace beside a missed-sample trace; no text.

## Slide 8
UNIT 5009 / WEEK 05 / LO2
10 MIN
LO2 FOUNDATIONS
Analogue signals and scaling
TEACHING POINTS
01
Analogue modules convert an input voltage or current to a raw digital value; the raw range, resolution, conversion time, and fault indications are specific to the module and configuration.
02
Clearly hypothetical linear example: a 4-20 mA transmitter represents 0-60 packs/min; 12 mA is halfway through the 16 mA span and therefore represents 30 packs/min if the transmitter and scaling are linear.
03
Scaling maps raw counts/current to engineering units; resolution is the smallest represented increment, while accuracy also includes sensor, module, wiring, and calibration error.
04
For a MedPack display, verify lower/upper range, units, underrange/overrange handling, and update time before treating a displayed value as a valid process measurement.
ANALOGUE SCALING
RAW ADC
ENGINEERING VALUE
Scale using configured range; resolution is not accuracy
SIGNAL PROCESSING AND SIGNAL INTEGRITY
08 / 18
Notes: Signal Processing and Signal Integrity | Week 05 | LO2 Slide 8 of 18 | Suggested time: 10 minutes | Criteria: LO2 foundations TEACHING NOTES AND ACTIVITY CUES 1. Analogue modules convert an input voltage or current to a raw digital value; the raw range, resolution, conversion time, and fault indications are specific to the module and configuration. 2. Clearly hypothetical linear example: a 4-20 mA transmitter represents 0-60 packs/min; 12 mA is halfway through the 16 mA span and therefore represents 30 packs/min if the transmitter and scaling are linear. 3. Scaling maps raw counts/current to engineering units; resolution is the smallest represented increment, while accuracy also includes sensor, module, wiring, and calibration error. 4. For a MedPack display, verify lower/upper range, units, underrange/overrange handling, and update time before treating a displayed value as a valid process measurement. TEACHING VISUAL The slide uses an editable analogue scaling diagram. Keep it unless the prompted image communicates the idea more clearly. OPTIONAL IMAGE PROMPT Original analogue signal diagram showing a 4-20 mA loop entering an ADC and a straight 0-60 packs-per-minute scaling line with a midpoint marker; no numbers, labels, or text.

## Slide 9
UNIT 5009 / WEEK 05 / LO2
15 MIN
LO2 FOUNDATIONS
Signal integrity and wiring practice
TEACHING POINTS
01
Noise can couple into sensor wiring through electromagnetic fields, shared impedance/reference paths, long cable runs, poor terminations, or switching inductive loads; symptoms may be intermittent counts or unstable analogue readings.
02
On a MedPack panel drawing, route low-level sensor wiring separately from motor/contactor conductors where the installation rules require it, and inspect cable type, terminal tightness, grounding/reference, and load suppression against manufacturer instructions.
03
Shield bonding is installation- and equipment-dependent; follow the PLC, sensor, and site EMC documentation rather than applying a universal one-end/both-ends rule.
04
Debrief: a filter may reduce brief disturbances but can also hide valid short pulses; correct routing, compatible interfaces, sound terminations, and a measured diagnosis come first.
SUGGESTED VISUAL
IMAGE SPACE
Insert the visual described in the speaker notes
SIGNAL PROCESSING AND SIGNAL INTEGRITY
09 / 18
Notes: Signal Processing and Signal Integrity | Week 05 | LO2 Slide 9 of 18 | Suggested time: 15 minutes | Criteria: LO2 foundations TEACHING NOTES AND ACTIVITY CUES 1. Noise can couple into sensor wiring through electromagnetic fields, shared impedance/reference paths, long cable runs, poor terminations, or switching inductive loads; symptoms may be intermittent counts or unstable analogue readings. 2. On a MedPack panel drawing, route low-level sensor wiring separately from motor/contactor conductors where the installation rules require it, and inspect cable type, terminal tightness, grounding/reference, and load suppression against manufacturer instructions. 3. Shield bonding is installation- and equipment-dependent; follow the PLC, sensor, and site EMC documentation rather than applying a universal one-end/both-ends rule. 4. Debrief: a filter may reduce brief disturbances but can also hide valid short pulses; correct routing, compatible interfaces, sound terminations, and a measured diagnosis come first. TEACHING VISUAL This slide has a reserved image bay. Add the image described below. OPTIONAL IMAGE PROMPT Original control-panel wiring photograph-style illustration with separated sensor and motor cable routes, a shielded sensor cable, terminal block, and inductive contactor load; no labels or text.

## Slide 10
UNIT 5009 / WEEK 05 / LO2
10 MIN
LO2 FOUNDATIONS
First-line troubleshooting flow
TEACHING POINTS
01
Procedure: confirm the safe test state and expected I/O map, then check supply and wiring, field-device indicator, terminal signal, input-channel indication, program tag, logic/filter, output-channel indication, and load in that order.
02
At each boundary record the expected state/value beside the observed one; the first mismatch narrows the fault to the interval since the previous confirmed-good point.
03
Example debrief: sensor LED changes but the PLC input LED does not, so investigate the cable, common/reference, terminal, channel configuration, and input circuit before editing count logic.
04
Never force an output or bypass a safety device on live equipment; use an authorised, risk-assessed test procedure and suitable isolation.
APPLICATION WORKFLOW
Sensor
Input filter
PLC logic
Actuator
Trace the requirement from the device to its verified result
SIGNAL PROCESSING AND SIGNAL INTEGRITY
10 / 18
Notes: Signal Processing and Signal Integrity | Week 05 | LO2 Slide 10 of 18 | Suggested time: 10 minutes | Criteria: LO2 foundations TEACHING NOTES AND ACTIVITY CUES 1. Procedure: confirm the safe test state and expected I/O map, then check supply and wiring, field-device indicator, terminal signal, input-channel indication, program tag, logic/filter, output-channel indication, and load in that order. 2. At each boundary record the expected state/value beside the observed one; the first mismatch narrows the fault to the interval since the previous confirmed-good point. 3. Example debrief: sensor LED changes but the PLC input LED does not, so investigate the cable, common/reference, terminal, channel configuration, and input circuit before editing count logic. 4. Never force an output or bypass a safety device on live equipment; use an authorised, risk-assessed test procedure and suitable isolation. TEACHING VISUAL The slide uses an editable application workflow diagram. Keep it unless the prompted image communicates the idea more clearly. OPTIONAL IMAGE PROMPT Original technician's fault-finding path through a sensor, terminal, PLC input LED, software tag monitor, output module, and actuator, with a meter used at a safe test point; no text.

## Slide 11
UNIT 5009 / WEEK 05 / LO2
10 MIN
LO2 FOUNDATIONS
Read the MedPack wiring diagram
TEACHING POINTS
01
Procedure: use the selected wiring diagram and I/O table to trace Start, Reset, pill sensor, actuator command, buzzer, and any E-stop status feedback from device terminal to PLC channel/tag.
02
Mark supply, common/reference, polarity, and output load type only after checking the selected sensor, CPU/module, and interface documentation; do not infer 24 V DC from a generic example.
03
Expected observation: each documented field signal has one traceable terminal/channel/tag assignment, while the safety circuit and any status-only feedback are visibly distinguished.
04
Ordinary HMI/SCADA or standard PLC logic must not be treated as the independent emergency-stop safety function; follow the training rig's safety design and local procedure.
SIGNAL PATH
SENSOR +
BUTTONS
PLC
INPUTS
CPU
LOGIC
OUTPUT
INTERFACE
ACTUATOR / BUZZER
Verify voltage, polarity, load current and channel limits
SIGNAL PROCESSING AND SIGNAL INTEGRITY
11 / 18
Notes: Signal Processing and Signal Integrity | Week 05 | LO2 Slide 11 of 18 | Suggested time: 10 minutes | Criteria: LO2 foundations TEACHING NOTES AND ACTIVITY CUES 1. Procedure: use the selected wiring diagram and I/O table to trace Start, Reset, pill sensor, actuator command, buzzer, and any E-stop status feedback from device terminal to PLC channel/tag. 2. Mark supply, common/reference, polarity, and output load type only after checking the selected sensor, CPU/module, and interface documentation; do not infer 24 V DC from a generic example. 3. Expected observation: each documented field signal has one traceable terminal/channel/tag assignment, while the safety circuit and any status-only feedback are visibly distinguished. 4. Ordinary HMI/SCADA or standard PLC logic must not be treated as the independent emergency-stop safety function; follow the training rig's safety design and local procedure. TEACHING VISUAL The slide uses an editable signal path diagram. Keep it unless the prompted image communicates the idea more clearly. OPTIONAL IMAGE PROMPT Original annotated-style electrical schematic layout with start/reset devices, photoelectric sensor, PLC I/O, relay-driven actuator and buzzer, plus a visually separate safety circuit; no text or symbols that resemble labels.

## Slide 12
UNIT 5009 / WEEK 05 / LO2
15 MIN
LO2 FOUNDATIONS
Map terminals to program tags
TEACHING POINTS
01
Procedure: inspect the actual CPU, slot/module order, channel configuration, terminal numbers, and project hardware tree before assigning each physical point to a symbolic tag.
02
For each MedPack input/output, record terminal, electrical type/polarity, normal state, tag name, logic use, and load/interface; distinguish a normally closed contact's healthy state from an asserted program bit.
03
Cross-check the wiring diagram, I/O schedule, and downloaded project; expected result is a one-to-one documented mapping with no assumed sample addresses.
SIGNAL PATH
SENSOR +
BUTTONS
PLC
INPUTS
CPU
LOGIC
OUTPUT
INTERFACE
ACTUATOR / BUZZER
Verify voltage, polarity, load current and channel limits
SIGNAL PROCESSING AND SIGNAL INTEGRITY
12 / 18
Notes: Signal Processing and Signal Integrity | Week 05 | LO2 Slide 12 of 18 | Suggested time: 15 minutes | Criteria: LO2 foundations TEACHING NOTES AND ACTIVITY CUES 1. Procedure: inspect the actual CPU, slot/module order, channel configuration, terminal numbers, and project hardware tree before assigning each physical point to a symbolic tag. 2. For each MedPack input/output, record terminal, electrical type/polarity, normal state, tag name, logic use, and load/interface; distinguish a normally closed contact's healthy state from an asserted program bit. 3. Cross-check the wiring diagram, I/O schedule, and downloaded project; expected result is a one-to-one documented mapping with no assumed sample addresses. TEACHING VISUAL The slide uses an editable signal path diagram. Keep it unless the prompted image communicates the idea more clearly. OPTIONAL IMAGE PROMPT Original split-view diagram linking a PLC rack channel and terminal strip to a software tag table using matching colored signal paths, without visible characters or text.

## Slide 13
UNIT 5009 / WEEK 05 / LO2
10 MIN
LO2 FOUNDATIONS
Demonstrate the normal operating cycle
TEACHING POINTS
01
Procedure on the authorised simulator/training rig: confirm safe idle, issue Start, generate one pill-sensor event at a time, observe count and state, reach the configured target, inspect the actuator/buzzer request, then reset using the documented sequence.
02
Expected observations: each valid event increments the count once; the target transition occurs at the configured value; outputs respond only when the program's permissives are true.
03
Monitor the physical/module indication and program tags together, and pause at each transition to explain which input or condition changed the state.
PROCESS STATE MODEL
READY
COUNT
PACKAGE
COMPLETE
FAULT / HOLD
Reset returns to ready only after the defined recovery checks
SIGNAL PROCESSING AND SIGNAL INTEGRITY
13 / 18
Notes: Signal Processing and Signal Integrity | Week 05 | LO2 Slide 13 of 18 | Suggested time: 10 minutes | Criteria: LO2 foundations TEACHING NOTES AND ACTIVITY CUES 1. Procedure on the authorised simulator/training rig: confirm safe idle, issue Start, generate one pill-sensor event at a time, observe count and state, reach the configured target, inspect the actuator/buzzer request, then reset using the documented sequence. 2. Expected observations: each valid event increments the count once; the target transition occurs at the configured value; outputs respond only when the program's permissives are true. 3. Monitor the physical/module indication and program tags together, and pause at each transition to explain which input or condition changed the state. TEACHING VISUAL The slide uses an editable process state model diagram. Keep it unless the prompted image communicates the idea more clearly. OPTIONAL IMAGE PROMPT Original training-rig scene with a pill sensor detecting individual sample tablets, PLC status LEDs, and an actuator indicator lamp during a cycle; no text or brand marks.

## Slide 14
UNIT 5009 / WEEK 05 / LO2
10 MIN
LO2 FOUNDATIONS
Observe, measure, and explain
TEACHING POINTS
01
Procedure: choose one sensor event and record its physical action, terminal-level signal, module indication, program tag, logic result, output indication, and load response in sequence.
02
Use an approved meter or simulator monitor at the designated test points; compare like-for-like voltage/current/state values and avoid probing live circuits outside the authorised method.
03
Expected debrief: if the terminal is correct but the channel/tag is not, inspect channel configuration or mapping; if the tag is correct but the output is not, inspect logic conditions and output assignment.
SIGNAL TIMING
RAW SENSOR: VALID EVENTS + CHATTER
QUALIFIED INPUT / ONE-SHOT EVENTS
Reject the short chatter; preserve all valid pill events
SIGNAL PROCESSING AND SIGNAL INTEGRITY
14 / 18
Notes: Signal Processing and Signal Integrity | Week 05 | LO2 Slide 14 of 18 | Suggested time: 10 minutes | Criteria: LO2 foundations TEACHING NOTES AND ACTIVITY CUES 1. Procedure: choose one sensor event and record its physical action, terminal-level signal, module indication, program tag, logic result, output indication, and load response in sequence. 2. Use an approved meter or simulator monitor at the designated test points; compare like-for-like voltage/current/state values and avoid probing live circuits outside the authorised method. 3. Expected debrief: if the terminal is correct but the channel/tag is not, inspect channel configuration or mapping; if the tag is correct but the output is not, inspect logic conditions and output assignment. TEACHING VISUAL The slide uses an editable signal timing diagram. Keep it unless the prompted image communicates the idea more clearly. OPTIONAL IMAGE PROMPT Original observation worksheet scene with a technician comparing a terminal meter reading, PLC input LED, software tag monitor, and output lamp; no text.

## Slide 15
UNIT 5009 / WEEK 05 / LO2
20 MIN
LO2 FOUNDATIONS
Fault case A: sensor chatter or stuck input
TEACHING POINTS
01
Procedure: in simulation or the approved de-energised/training setup, select chatter, stuck-high, or stuck-low; record the initial filter/edge settings and predict the count/status before applying the fault.
02
Apply the fault, observe sensor/channel/tag/count and any diagnostic, then identify the first point where behaviour differs from expectation; do not alter wiring on an energised rig unless the approved procedure allows it.
03
Correct the cause using documented mapping, edge logic, filter, or sensor/wiring checks; repeat the same input sequence and compare before/after results.
04
Expected debrief: chatter may create extra edges, a stuck-high may produce only one edge then no further counts, and stuck-low produces no event; final behaviour depends on the configured program and diagnostics.
SUGGESTED VISUAL
IMAGE SPACE
Insert the visual described in the speaker notes
SIGNAL PROCESSING AND SIGNAL INTEGRITY
15 / 18
Notes: Signal Processing and Signal Integrity | Week 05 | LO2 Slide 15 of 18 | Suggested time: 20 minutes | Criteria: LO2 foundations TEACHING NOTES AND ACTIVITY CUES 1. Procedure: in simulation or the approved de-energised/training setup, select chatter, stuck-high, or stuck-low; record the initial filter/edge settings and predict the count/status before applying the fault. 2. Apply the fault, observe sensor/channel/tag/count and any diagnostic, then identify the first point where behaviour differs from expectation; do not alter wiring on an energised rig unless the approved procedure allows it. 3. Correct the cause using documented mapping, edge logic, filter, or sensor/wiring checks; repeat the same input sequence and compare before/after results. 4. Expected debrief: chatter may create extra edges, a stuck-high may produce only one edge then no further counts, and stuck-low produces no event; final behaviour depends on the configured program and diagnostics. TEACHING VISUAL This slide has a reserved image bay. Add the image described below. OPTIONAL IMAGE PROMPT Original fault-injection training diagram showing a simulated bouncing sensor input, a PLC trend monitor, and a before/after count trace; no embedded text.

## Slide 16
UNIT 5009 / WEEK 05 / LO2
20 MIN
LO2 FOUNDATIONS
Fault case B: E-stop and output response
TEACHING POINTS
01
Procedure: under the instructor's authorised rig procedure, verify the E-stop device and safety design before testing; actuate it and observe the designed safe response, then inspect standard PLC status feedback and alarm indication separately.
02
Expected observation: the safety function reaches its specified safe state independently of ordinary HMI/SCADA availability; a standard PLC tag may report status but is not proof of a safety-rated action.
03
Check reset and restart permissives: releasing/resetting the E-stop must not itself cause an unexpected automatic restart; follow the actual safety relay/controller documentation.
04
Keep buzzer/fault handling distinct from the safety function, and never simulate by bypassing or defeating an E-stop circuit.
SAFE RESPONSE PATH
KEEP THE SAFETY FUNCTION DISTINCT
E-STOP
DEVICE
SAFETY
RELAY / PLC
HAZARDOUS
ENERGY
STANDARD PLC: STATUS MONITORING
Risk assessment defines the required architecture and reset behaviour
SIGNAL PROCESSING AND SIGNAL INTEGRITY
16 / 18
Notes: Signal Processing and Signal Integrity | Week 05 | LO2 Slide 16 of 18 | Suggested time: 20 minutes | Criteria: LO2 foundations TEACHING NOTES AND ACTIVITY CUES 1. Procedure: under the instructor's authorised rig procedure, verify the E-stop device and safety design before testing; actuate it and observe the designed safe response, then inspect standard PLC status feedback and alarm indication separately. 2. Expected observation: the safety function reaches its specified safe state independently of ordinary HMI/SCADA availability; a standard PLC tag may report status but is not proof of a safety-rated action. 3. Check reset and restart permissives: releasing/resetting the E-stop must not itself cause an unexpected automatic restart; follow the actual safety relay/controller documentation. 4. Keep buzzer/fault handling distinct from the safety function, and never simulate by bypassing or defeating an E-stop circuit. TEACHING VISUAL The slide uses an editable safe response path diagram. Keep it unless the prompted image communicates the idea more clearly. OPTIONAL IMAGE PROMPT Original safety-training panel showing a mushroom emergency-stop actuator, separate safety relay path, standard PLC status input, and de-energised actuator interface; no text.

## Slide 17
UNIT 5009 / WEEK 05 / LO2
7 MIN
LO2 FOUNDATIONS
Lab-record quality review
TEACHING POINTS
01
Check the dated record identifies the rig/PLC configuration, project version, wiring diagram, I/O map, test conditions, and safe test method.
02
Confirm each test has a reproducible procedure, predicted result, measured/observed result, diagnosis, corrective action, and retest outcome.
03
Expected review finding: a screenshot or trend without setup, tag/address context, or expected-versus-observed comparison is not sufficient to reproduce the test.
FORMATIVE CHECK
01
EXPECTED STATE
02
MEASURE SIGNAL
03
FIND BOUNDARY
04
RETEST + RECORD
SIGNAL PROCESSING AND SIGNAL INTEGRITY
17 / 18
Notes: Signal Processing and Signal Integrity | Week 05 | LO2 Slide 17 of 18 | Suggested time: 7 minutes | Criteria: LO2 foundations TEACHING NOTES AND ACTIVITY CUES 1. Check the dated record identifies the rig/PLC configuration, project version, wiring diagram, I/O map, test conditions, and safe test method. 2. Confirm each test has a reproducible procedure, predicted result, measured/observed result, diagnosis, corrective action, and retest outcome. 3. Expected review finding: a screenshot or trend without setup, tag/address context, or expected-versus-observed comparison is not sufficient to reproduce the test. TEACHING VISUAL The slide uses an editable formative check diagram. Keep it unless the prompted image communicates the idea more clearly. OPTIONAL IMAGE PROMPT Original close-up of a neat engineering lab notebook beside a PLC training rig and annotated signal trace, with blank pages and no readable text.

## Slide 18
UNIT 5009 / WEEK 05 / LO2
8 MIN
LO2 FOUNDATIONS
Exit ticket: diagnose the first boundary
TEACHING POINTS
01
Given a sensor LED that changes while the PLC input indication stays off, identify the terminal/channel boundary as the next check and give one plausible cause such as wiring, reference, configuration, or channel fault.
02
State that input filtering can reject short unwanted transitions, but an excessive setting can suppress valid short pulses and delay response.
03
Hand in one concise answer with the test point, expected observation, and evidence that would distinguish the likely causes.
FORMATIVE CHECK
01
EXPECTED STATE
02
MEASURE SIGNAL
03
FIND BOUNDARY
04
RETEST + RECORD
SIGNAL PROCESSING AND SIGNAL INTEGRITY
18 / 18
Notes: Signal Processing and Signal Integrity | Week 05 | LO2 Slide 18 of 18 | Suggested time: 8 minutes | Criteria: LO2 foundations TEACHING NOTES AND ACTIVITY CUES 1. Given a sensor LED that changes while the PLC input indication stays off, identify the terminal/channel boundary as the next check and give one plausible cause such as wiring, reference, configuration, or channel fault. 2. State that input filtering can reject short unwanted transitions, but an excessive setting can suppress valid short pulses and delay response. 3. Hand in one concise answer with the test point, expected observation, and evidence that would distinguish the likely causes. TEACHING VISUAL The slide uses an editable formative check diagram. Keep it unless the prompted image communicates the idea more clearly. OPTIONAL IMAGE PROMPT Original simple diagnostic decision path beginning with a lit sensor indicator and an unlit PLC input indicator, ending at a terminal measurement point; no text.