## Slide 1
UNIT 5009 / WEEK 06 / LO2
5 MIN
P3
Signal processing retrieval
TEACHING POINTS
01
Reconstruct the Week 5 path: pill sensor -> PLC input -> count logic -> output interface -> actuator request; identify where a communication link is actually present.
02
A local sensor wired to a PLC input has an electrical signal path, not automatically a network protocol; remote I/O or an HMI connection adds a configured communication connection.
03
Expected answer: on the Week 7-style architecture, label the cable/interface separately from the protocol used to exchange PLC data.
SUGGESTED VISUAL
IMAGE SPACE
Insert the visual described in the speaker notes
COMMUNICATION LINKS AND PLC PROTOCOLS
01 / 18
Notes: Communication Links and PLC Protocols | Week 06 | LO2 Slide 1 of 18 | Suggested time: 5 minutes | Criteria: P3 TEACHING NOTES AND ACTIVITY CUES 1. Reconstruct the Week 5 path: pill sensor -> PLC input -> count logic -> output interface -> actuator request; identify where a communication link is actually present. 2. A local sensor wired to a PLC input has an electrical signal path, not automatically a network protocol; remote I/O or an HMI connection adds a configured communication connection. 3. Expected answer: on the Week 7-style architecture, label the cable/interface separately from the protocol used to exchange PLC data. TEACHING VISUAL This slide has a reserved image bay. Add the image described below. OPTIONAL IMAGE PROMPT Original MedPack signal-chain diagram with a local sensor wire and a separate PLC-to-HMI network cable highlighted in different colors; no labels or text.

## Slide 2
UNIT 5009 / WEEK 06 / LO2
5 MIN
P3
Link or protocol?
TEACHING POINTS
01
Classify Ethernet as a family of link/physical-layer technologies, RS-485 as an electrical interface, Modbus RTU and Modbus TCP as protocol variants, and PROFINET as an industrial communication system/protocol family.
02
Modbus RTU commonly runs over serial interfaces such as RS-485, while Modbus TCP commonly runs over TCP/IP on Ethernet; the cable/interface alone does not determine the application protocol.
03
Expected correction: calling RS-485 a protocol or assuming every Ethernet device speaks the same PLC protocol confuses different layers.
COMMUNICATION ARCHITECTURE
SWITCHED ETHERNET
PLC
SWITCH
HMI
SERIAL RS-485 TRUNK
PLC
NODE
NODE
The link and protocol are separate choices
COMMUNICATION LINKS AND PLC PROTOCOLS
02 / 18
Notes: Communication Links and PLC Protocols | Week 06 | LO2 Slide 2 of 18 | Suggested time: 5 minutes | Criteria: P3 TEACHING NOTES AND ACTIVITY CUES 1. Classify Ethernet as a family of link/physical-layer technologies, RS-485 as an electrical interface, Modbus RTU and Modbus TCP as protocol variants, and PROFINET as an industrial communication system/protocol family. 2. Modbus RTU commonly runs over serial interfaces such as RS-485, while Modbus TCP commonly runs over TCP/IP on Ethernet; the cable/interface alone does not determine the application protocol. 3. Expected correction: calling RS-485 a protocol or assuming every Ethernet device speaks the same PLC protocol confuses different layers. TEACHING VISUAL The slide uses an editable communication architecture diagram. Keep it unless the prompted image communicates the idea more clearly. OPTIONAL IMAGE PROMPT Original five-object sorting illustration: copper Ethernet cable, RS-485 differential pair, serial frame, TCP/IP packet, and industrial PLC network device, arranged in physical-versus-protocol groups without text.

## Slide 3
UNIT 5009 / WEEK 06 / LO2
5 MIN
P3
P3 success criteria
TEACHING POINTS
01
LO2.P3 requires an illustrated comparison of at least two communication links/interfaces and at least two PLC-relevant standards or protocols.
02
For each example, learners should identify topology/distance, noise considerations, speed or bandwidth qualitatively, and a typical use case, with numeric limits sourced from the selected equipment manual.
03
Evidence for today is a comparison matrix plus a labelled connection diagram; a list of names without layer distinction does not demonstrate the criterion.
FORMATIVE CHECK
01
PHYSICAL LINK
02
PROTOCOL
03
ENDPOINT MAP
04
SOURCE / LIMIT
COMMUNICATION LINKS AND PLC PROTOCOLS
03 / 18
Notes: Communication Links and PLC Protocols | Week 06 | LO2 Slide 3 of 18 | Suggested time: 5 minutes | Criteria: P3 TEACHING NOTES AND ACTIVITY CUES 1. LO2.P3 requires an illustrated comparison of at least two communication links/interfaces and at least two PLC-relevant standards or protocols. 2. For each example, learners should identify topology/distance, noise considerations, speed or bandwidth qualitatively, and a typical use case, with numeric limits sourced from the selected equipment manual. 3. Evidence for today is a comparison matrix plus a labelled connection diagram; a list of names without layer distinction does not demonstrate the criterion. TEACHING VISUAL The slide uses an editable formative check diagram. Keep it unless the prompted image communicates the idea more clearly. OPTIONAL IMAGE PROMPT Original teaching-board composition showing two side-by-side PLC communication paths and a blank comparison matrix, with diagrams only and no writing.

## Slide 4
UNIT 5009 / WEEK 06 / LO2
12 MIN
P3
Communication layers in practical terms
TEACHING POINTS
01
Separate the cable/medium and electrical interface, network topology, addressing, transport service, and application-level data rules; each answers a different commissioning question.
02
Worked MedPack path: twisted-pair copper Ethernet connects PLC and HMI through switches, IP addressing identifies endpoints, TCP transports a Modbus TCP exchange, and the Modbus data model identifies values.
03
RS-485 specifies electrical signalling characteristics, not the meaning or register map of the message; Modbus RTU is one protocol that may use that interface.
04
Check each device manual for supported physical interfaces, protocol roles, addressing, and services before declaring two devices compatible.
COMMUNICATION ARCHITECTURE
PLC
CONTROLLER
LOCAL I/O
REMOTE I/O
HMI
SCADA
Label the medium and protocol on every connection
COMMUNICATION LINKS AND PLC PROTOCOLS
04 / 18
Notes: Communication Links and PLC Protocols | Week 06 | LO2 Slide 4 of 18 | Suggested time: 12 minutes | Criteria: P3 TEACHING NOTES AND ACTIVITY CUES 1. Separate the cable/medium and electrical interface, network topology, addressing, transport service, and application-level data rules; each answers a different commissioning question. 2. Worked MedPack path: twisted-pair copper Ethernet connects PLC and HMI through switches, IP addressing identifies endpoints, TCP transports a Modbus TCP exchange, and the Modbus data model identifies values. 3. RS-485 specifies electrical signalling characteristics, not the meaning or register map of the message; Modbus RTU is one protocol that may use that interface. 4. Check each device manual for supported physical interfaces, protocol roles, addressing, and services before declaring two devices compatible. TEACHING VISUAL The slide uses an editable communication architecture diagram. Keep it unless the prompted image communicates the idea more clearly. OPTIONAL IMAGE PROMPT Original layered communications stack illustrated as a physical copper path, switch network, endpoint addresses, transport envelope, and PLC data table, with no text or labels.

## Slide 5
UNIT 5009 / WEEK 06 / LO2
13 MIN
P3
Industrial Ethernet connections
TEACHING POINTS
01
Industrial Ethernet installations may use copper or fibre media and managed/unmanaged switches; exact cable category, connectors, segment limits, and environmental rating come from the installed equipment specifications.
02
Star, line, and ring describe possible physical/logical arrangements; a ring provides redundancy only when devices and the configured protocol/recovery mechanism support it.
03
Ethernet does not guarantee deterministic timing by itself: traffic, switch configuration, protocol, device load, and engineered QoS/redundancy affect performance and recovery.
04
For MedPack, trace PLC, HMI, remote I/O, and engineering port connections, then mark the actual switch boundaries and any supported diagnostics or redundancy.
COMMUNICATION ARCHITECTURE
SWITCHED ETHERNET
PLC
SWITCH
HMI
SERIAL RS-485 TRUNK
PLC
NODE
NODE
The link and protocol are separate choices
COMMUNICATION LINKS AND PLC PROTOCOLS
05 / 18
Notes: Communication Links and PLC Protocols | Week 06 | LO2 Slide 5 of 18 | Suggested time: 13 minutes | Criteria: P3 TEACHING NOTES AND ACTIVITY CUES 1. Industrial Ethernet installations may use copper or fibre media and managed/unmanaged switches; exact cable category, connectors, segment limits, and environmental rating come from the installed equipment specifications. 2. Star, line, and ring describe possible physical/logical arrangements; a ring provides redundancy only when devices and the configured protocol/recovery mechanism support it. 3. Ethernet does not guarantee deterministic timing by itself: traffic, switch configuration, protocol, device load, and engineered QoS/redundancy affect performance and recovery. 4. For MedPack, trace PLC, HMI, remote I/O, and engineering port connections, then mark the actual switch boundaries and any supported diagnostics or redundancy. TEACHING VISUAL The slide uses an editable communication architecture diagram. Keep it unless the prompted image communicates the idea more clearly. OPTIONAL IMAGE PROMPT Original industrial control cabinet scene showing copper Ethernet patch leads to a switch, one fibre uplink, a PLC, HMI, and remote-I/O drop; no labels, logos, or text.

## Slide 6
UNIT 5009 / WEEK 06 / LO2
12 MIN
P3
Serial interfaces: RS-232 and RS-485
TEACHING POINTS
01
RS-232 is commonly used for a point-to-point serial connection; RS-485 uses differential signalling and can support multi-drop networks when transceivers, topology, and device loading are designed accordingly.
02
RS-485 does not define Modbus or any other message format; a PLC and device need matching serial settings and a shared supported protocol such as Modbus RTU.
03
Follow the selected transceiver/device manuals for cable, polarity, termination, biasing, node loading, segment length, and grounding; avoid adding termination or bias by guesswork.
04
Commissioning procedure: verify interface and pinout, baud/parity/stop bits, node addresses, wiring polarity, and end-of-line requirements; expected result is stable replies from the intended node without unexplained retries.
SUGGESTED VISUAL
IMAGE SPACE
Insert the visual described in the speaker notes
COMMUNICATION LINKS AND PLC PROTOCOLS
06 / 18
Notes: Communication Links and PLC Protocols | Week 06 | LO2 Slide 6 of 18 | Suggested time: 12 minutes | Criteria: P3 TEACHING NOTES AND ACTIVITY CUES 1. RS-232 is commonly used for a point-to-point serial connection; RS-485 uses differential signalling and can support multi-drop networks when transceivers, topology, and device loading are designed accordingly. 2. RS-485 does not define Modbus or any other message format; a PLC and device need matching serial settings and a shared supported protocol such as Modbus RTU. 3. Follow the selected transceiver/device manuals for cable, polarity, termination, biasing, node loading, segment length, and grounding; avoid adding termination or bias by guesswork. 4. Commissioning procedure: verify interface and pinout, baud/parity/stop bits, node addresses, wiring polarity, and end-of-line requirements; expected result is stable replies from the intended node without unexplained retries. TEACHING VISUAL This slide has a reserved image bay. Add the image described below. OPTIONAL IMAGE PROMPT Original comparison diagram showing a two-wire RS-232 point-to-point path beside a differential RS-485 trunk with correctly placed end termination and several PLC devices; no text.

## Slide 7
UNIT 5009 / WEEK 06 / LO2
13 MIN
P3
What changes the link choice?
TEACHING POINTS
01
Start with requirements: number/type of devices, cable route and distance, update needs, noise environment, topology, existing infrastructure, diagnostics, maintenance skills, and lifecycle support.
02
Clearly hypothetical case: a panel 40 m from a sensor bank with eight devices is a requirements prompt, not a universal Ethernet/RS-485 distance rule; compare supported PLC interfaces and device protocol maps before choosing.
03
A link decision does not establish application compatibility: confirm both endpoints support the same protocol role, data model, configuration tools, and required services.
04
Expected justification names one advantage and one constraint for the proposed MedPack connection and cites the source for any numeric cable or performance limit.
DECISION METHOD
FIRST: PASS / FAIL MANDATORY GATES
Electrical fit
PASS
FAIL = EXCLUDE
Required I/O
PASS
FAIL = EXCLUDE
Safety boundary
PASS
FAIL = EXCLUDE
THEN weigh preferences with cited evidence
COMMUNICATION LINKS AND PLC PROTOCOLS
07 / 18
Notes: Communication Links and PLC Protocols | Week 06 | LO2 Slide 7 of 18 | Suggested time: 13 minutes | Criteria: P3 TEACHING NOTES AND ACTIVITY CUES 1. Start with requirements: number/type of devices, cable route and distance, update needs, noise environment, topology, existing infrastructure, diagnostics, maintenance skills, and lifecycle support. 2. Clearly hypothetical case: a panel 40 m from a sensor bank with eight devices is a requirements prompt, not a universal Ethernet/RS-485 distance rule; compare supported PLC interfaces and device protocol maps before choosing. 3. A link decision does not establish application compatibility: confirm both endpoints support the same protocol role, data model, configuration tools, and required services. 4. Expected justification names one advantage and one constraint for the proposed MedPack connection and cites the source for any numeric cable or performance limit. TEACHING VISUAL The slide uses an editable decision method diagram. Keep it unless the prompted image communicates the idea more clearly. OPTIONAL IMAGE PROMPT Original engineering planning scene showing a PLC panel, distant sensor bank, alternative copper and serial routes, and a noise source near a motor cable; no annotations or text.

## Slide 8
UNIT 5009 / WEEK 06 / LO2
10 MIN
P3
Link comparison table
TEACHING POINTS
01
Fill the table with a specific Ethernet implementation and a specific serial interface (for example, copper switched Ethernet versus two-wire RS-485), not generic labels alone.
02
Compare physical medium/interface, supported topology, installation/noise controls, likely PLC use, diagnostics, and maintenance; state which details depend on product design.
03
Qualitative comparison is acceptable where the hardware is not yet selected; any speed, node-count, or distance figure must cite the relevant interface/device manual.
04
Expected debrief: no link is universally faster, longer-range, or more noise-immune without its medium, transceivers, network design, and operating conditions being specified.
COMPARISON FRAMEWORK
LAYER
EXAMPLE A
EXAMPLE B
Physical
Ethernet
RS-485
Protocol
Modbus TCP
Modbus RTU
Topology
Switched LAN
Serial bus
Evidence
Device manual
Device manual
Use exact model manuals; do not infer missing specifications
COMMUNICATION LINKS AND PLC PROTOCOLS
08 / 18
Notes: Communication Links and PLC Protocols | Week 06 | LO2 Slide 8 of 18 | Suggested time: 10 minutes | Criteria: P3 TEACHING NOTES AND ACTIVITY CUES 1. Fill the table with a specific Ethernet implementation and a specific serial interface (for example, copper switched Ethernet versus two-wire RS-485), not generic labels alone. 2. Compare physical medium/interface, supported topology, installation/noise controls, likely PLC use, diagnostics, and maintenance; state which details depend on product design. 3. Qualitative comparison is acceptable where the hardware is not yet selected; any speed, node-count, or distance figure must cite the relevant interface/device manual. 4. Expected debrief: no link is universally faster, longer-range, or more noise-immune without its medium, transceivers, network design, and operating conditions being specified. TEACHING VISUAL The slide uses an editable comparison framework diagram. Keep it unless the prompted image communicates the idea more clearly. OPTIONAL IMAGE PROMPT Original blank comparison chart beside a copper Ethernet switch and RS-485 terminal bus, with visual cues for topology, cable, and diagnostics but no words or numbers.

## Slide 9
UNIT 5009 / WEEK 06 / LO2
15 MIN
P3
Standards and protocols are not the cable
TEACHING POINTS
01
One Ethernet installation can carry different protocol traffic, but each endpoint must implement the same protocol and compatible roles/configuration; shared cabling is not protocol interoperability.
02
Example pairs: Modbus RTU over a supported serial interface such as RS-485; Modbus TCP over TCP/IP and Ethernet; PROFINET and EtherNet/IP use industrial Ethernet infrastructure with distinct device/configuration ecosystems.
03
Distinguish a protocol from its transport and medium: changing the cable does not translate registers, device profiles, or cyclic-I/O services.
04
Ask learners to identify the evidence needed before connecting a PLC and HMI: supported protocol on both devices, role, address/data map, configuration, and version/option constraints.
PROTOCOL COMPARISON
PROFINET
Industrial Ethernet family
Device/configuration model
Verify controller role
EtherNet/IP
Industrial Ethernet family
Distinct configuration model
Verify scanner/adapter role
Ethernet cabling does not make the protocol families interchangeable
COMMUNICATION LINKS AND PLC PROTOCOLS
09 / 18
Notes: Communication Links and PLC Protocols | Week 06 | LO2 Slide 9 of 18 | Suggested time: 15 minutes | Criteria: P3 TEACHING NOTES AND ACTIVITY CUES 1. One Ethernet installation can carry different protocol traffic, but each endpoint must implement the same protocol and compatible roles/configuration; shared cabling is not protocol interoperability. 2. Example pairs: Modbus RTU over a supported serial interface such as RS-485; Modbus TCP over TCP/IP and Ethernet; PROFINET and EtherNet/IP use industrial Ethernet infrastructure with distinct device/configuration ecosystems. 3. Distinguish a protocol from its transport and medium: changing the cable does not translate registers, device profiles, or cyclic-I/O services. 4. Ask learners to identify the evidence needed before connecting a PLC and HMI: supported protocol on both devices, role, address/data map, configuration, and version/option constraints. TEACHING VISUAL The slide uses an editable protocol comparison diagram. Keep it unless the prompted image communicates the idea more clearly. OPTIONAL IMAGE PROMPT Original diagram showing one Ethernet switch carrying two visually distinct PLC-HMI communication paths to compatible endpoints, plus an isolated serial Modbus RTU path; no text.

## Slide 10
UNIT 5009 / WEEK 06 / LO2
10 MIN
P3
P3 comparison prompt
TEACHING POINTS
01
Activity procedure: teams select a MedPack PLC-to-HMI requirement card, list the endpoints and needed data, and choose one supported link/interface plus one protocol pairing.
02
Compare the choice with an alternative on topology/distance, noise/installation, speed or update needs, typical use, and commissioning support; label unknowns instead of inventing specifications.
03
Expected response: recommend a compatible pair only after checking both endpoint manuals and the register/tag mapping, then state a limitation and one condition that could change the choice.
COMPARISON FRAMEWORK
LAYER
EXAMPLE A
EXAMPLE B
Physical
Ethernet
RS-485
Protocol
Modbus TCP
Modbus RTU
Topology
Switched LAN
Serial bus
Evidence
Device manual
Device manual
Use exact model manuals; do not infer missing specifications
COMMUNICATION LINKS AND PLC PROTOCOLS
10 / 18
Notes: Communication Links and PLC Protocols | Week 06 | LO2 Slide 10 of 18 | Suggested time: 10 minutes | Criteria: P3 TEACHING NOTES AND ACTIVITY CUES 1. Activity procedure: teams select a MedPack PLC-to-HMI requirement card, list the endpoints and needed data, and choose one supported link/interface plus one protocol pairing. 2. Compare the choice with an alternative on topology/distance, noise/installation, speed or update needs, typical use, and commissioning support; label unknowns instead of inventing specifications. 3. Expected response: recommend a compatible pair only after checking both endpoint manuals and the register/tag mapping, then state a limitation and one condition that could change the choice. TEACHING VISUAL The slide uses an editable comparison framework diagram. Keep it unless the prompted image communicates the idea more clearly. OPTIONAL IMAGE PROMPT Original small-team engineering workshop scene with a PLC, HMI, Ethernet switch, serial gateway, and a blank requirement card being compared; no readable text.

## Slide 11
UNIT 5009 / WEEK 06 / LO2
10 MIN
P3
Modbus RTU and Modbus TCP
TEACHING POINTS
01
Modbus RTU commonly carries framed requests over serial links; Modbus TCP carries Modbus application messages over TCP/IP, commonly on Ethernet. The serial and TCP transport details differ even when the data model is familiar.
02
The common data model distinguishes coils and discrete inputs (bit values) from holding and input registers (16-bit values); read/write permissions and device-specific support vary.
03
Worked mapping: a MedPack PillCount may be represented by a documented register or tag, but the actual address, signedness, scaling, word order, and allowed function code must come from the PLC map.
04
Check reference notation versus client indexing with both PLC and client documentation; a displayed 40001 reference may be represented by a zero-based software offset, but this is not universal.
PROTOCOL COMPARISON
MODBUS RTU
Serial message framing
Device/node address
Commonly over serial
MODBUS TCP
TCP/IP transport
IP endpoint
Commonly over Ethernet
Same familiar data concepts; transport and addressing differ
COMMUNICATION LINKS AND PLC PROTOCOLS
11 / 18
Notes: Communication Links and PLC Protocols | Week 06 | LO2 Slide 11 of 18 | Suggested time: 10 minutes | Criteria: P3 TEACHING NOTES AND ACTIVITY CUES 1. Modbus RTU commonly carries framed requests over serial links; Modbus TCP carries Modbus application messages over TCP/IP, commonly on Ethernet. The serial and TCP transport details differ even when the data model is familiar. 2. The common data model distinguishes coils and discrete inputs (bit values) from holding and input registers (16-bit values); read/write permissions and device-specific support vary. 3. Worked mapping: a MedPack PillCount may be represented by a documented register or tag, but the actual address, signedness, scaling, word order, and allowed function code must come from the PLC map. 4. Check reference notation versus client indexing with both PLC and client documentation; a displayed 40001 reference may be represented by a zero-based software offset, but this is not universal. TEACHING VISUAL The slide uses an editable protocol comparison diagram. Keep it unless the prompted image communicates the idea more clearly. OPTIONAL IMAGE PROMPT Original side-by-side Modbus RTU serial frame and Modbus TCP message path, with a coil bit and 16-bit register drawn as data examples but no characters or text.

## Slide 12
UNIT 5009 / WEEK 06 / LO2
15 MIN
P3
PROFINET and EtherNet/IP
TEACHING POINTS
01
PROFINET and EtherNet/IP are distinct industrial communication systems that use Ethernet infrastructure but have different device descriptions, configuration workflows, services, and interoperability requirements.
02
At a high level, both support time-sensitive cyclic data exchange and additional configuration/diagnostic or explicit services, but the exact mechanisms and timing depend on protocol variant, device, controller, and network design.
03
For a MedPack PLC/HMI/device combination, verify the CPU/module role, firmware/options, supported device profile, configuration file, data size, diagnostic coverage, and vendor compatibility in current manuals.
04
Neither name is a generic synonym for Ethernet; ordinary Ethernet connectivity alone does not prove the PLC can exchange the required process data.
PROTOCOL COMPARISON
PROFINET
Industrial Ethernet family
Device/configuration model
Verify controller role
EtherNet/IP
Industrial Ethernet family
Distinct configuration model
Verify scanner/adapter role
Ethernet cabling does not make the protocol families interchangeable
COMMUNICATION LINKS AND PLC PROTOCOLS
12 / 18
Notes: Communication Links and PLC Protocols | Week 06 | LO2 Slide 12 of 18 | Suggested time: 15 minutes | Criteria: P3 TEACHING NOTES AND ACTIVITY CUES 1. PROFINET and EtherNet/IP are distinct industrial communication systems that use Ethernet infrastructure but have different device descriptions, configuration workflows, services, and interoperability requirements. 2. At a high level, both support time-sensitive cyclic data exchange and additional configuration/diagnostic or explicit services, but the exact mechanisms and timing depend on protocol variant, device, controller, and network design. 3. For a MedPack PLC/HMI/device combination, verify the CPU/module role, firmware/options, supported device profile, configuration file, data size, diagnostic coverage, and vendor compatibility in current manuals. 4. Neither name is a generic synonym for Ethernet; ordinary Ethernet connectivity alone does not prove the PLC can exchange the required process data. TEACHING VISUAL The slide uses an editable protocol comparison diagram. Keep it unless the prompted image communicates the idea more clearly. OPTIONAL IMAGE PROMPT Original two distinct industrial PLC network diagrams, one with a controller and configured I/O device and one with a scanner/adapter pair, both connected through Ethernet switches; no text or logos.

## Slide 13
UNIT 5009 / WEEK 06 / LO2
10 MIN
P3
Other PLC-relevant technologies
TEACHING POINTS
01
PROFIBUS is a fieldbus family used for controller/device communication; IO-Link is a point-to-point sensor/actuator interface through an IO-Link master; OPC UA provides structured information exchange between compatible applications/devices.
02
MedPack examples: a supported PROFIBUS remote-I/O segment, an IO-Link smart sensor connected to a compatible master, or OPC UA data exposure to a supervisory client are different integration points, not interchangeable cable choices.
03
For each candidate, identify the master/controller/client role, device support, required gateway or module, configuration tools, data model, and security/update constraints.
04
Expected response: choose the technology that matches the integration need, then verify the actual PLC module and device protocol maps before promising connectivity.
TECHNOLOGY ROLES
PROFIBUS
Fieldbus
controller / device
IO-LINK
Sensor / actuator
via a master
OPC UA
Structured
information exchange
Different roles: verify device support, module and data model
COMMUNICATION LINKS AND PLC PROTOCOLS
13 / 18
Notes: Communication Links and PLC Protocols | Week 06 | LO2 Slide 13 of 18 | Suggested time: 10 minutes | Criteria: P3 TEACHING NOTES AND ACTIVITY CUES 1. PROFIBUS is a fieldbus family used for controller/device communication; IO-Link is a point-to-point sensor/actuator interface through an IO-Link master; OPC UA provides structured information exchange between compatible applications/devices. 2. MedPack examples: a supported PROFIBUS remote-I/O segment, an IO-Link smart sensor connected to a compatible master, or OPC UA data exposure to a supervisory client are different integration points, not interchangeable cable choices. 3. For each candidate, identify the master/controller/client role, device support, required gateway or module, configuration tools, data model, and security/update constraints. 4. Expected response: choose the technology that matches the integration need, then verify the actual PLC module and device protocol maps before promising connectivity. TEACHING VISUAL The slide uses an editable technology roles diagram. Keep it unless the prompted image communicates the idea more clearly. OPTIONAL IMAGE PROMPT Original three-panel industrial illustration of a PROFIBUS fieldbus segment, an IO-Link master with smart sensor, and an OPC UA server-client information path; no text.

## Slide 14
UNIT 5009 / WEEK 06 / LO2
10 MIN
P3
Data mapping, quality, and permissions
TEACHING POINTS
01
Trace one MedPack value end-to-end: PLC tag -> verified protocol address or symbol -> data type/encoding -> HMI display, documenting units and any scaling.
02
Use PillCount as an integer read value and StartRequest as a bounded command request; define range, ownership, read/write permission, update expectation, and stale/quality indication for each.
03
Check byte/word order for multi-register values, signedness, address offsets, and data update rate using both endpoint documentation and a known-value test.
04
EStopStatusReadOnly may be displayed as status feedback only; HMI data mapping is not a substitute for the independent safety function.
SIGNAL PATH
SENSOR +
BUTTONS
PLC
INPUTS
CPU
LOGIC
OUTPUT
INTERFACE
ACTUATOR / BUZZER
Verify voltage, polarity, load current and channel limits
COMMUNICATION LINKS AND PLC PROTOCOLS
14 / 18
Notes: Communication Links and PLC Protocols | Week 06 | LO2 Slide 14 of 18 | Suggested time: 10 minutes | Criteria: P3 TEACHING NOTES AND ACTIVITY CUES 1. Trace one MedPack value end-to-end: PLC tag -> verified protocol address or symbol -> data type/encoding -> HMI display, documenting units and any scaling. 2. Use PillCount as an integer read value and StartRequest as a bounded command request; define range, ownership, read/write permission, update expectation, and stale/quality indication for each. 3. Check byte/word order for multi-register values, signedness, address offsets, and data update rate using both endpoint documentation and a known-value test. 4. EStopStatusReadOnly may be displayed as status feedback only; HMI data mapping is not a substitute for the independent safety function. TEACHING VISUAL The slide uses an editable signal path diagram. Keep it unless the prompted image communicates the idea more clearly. OPTIONAL IMAGE PROMPT Original tag-mapping diagram connecting a PLC variable table through a protocol data block to an HMI numeric display and a permission-controlled command button; no labels or text.

## Slide 15
UNIT 5009 / WEEK 06 / LO2
20 MIN
P3
Build the P3 comparison matrix
TEACHING POINTS
01
Activity procedure: create two separate matrix sections, comparing a specified Ethernet/serial interface pair and Modbus TCP/RTU protocol variants; do not place protocol names in the physical-link column.
02
For each option record topology, distance constraints, noise/installation considerations, bandwidth/update suitability, typical PLC use, commissioning strengths, and limits.
03
Add one documented MedPack endpoint pair and cite official manuals for all numeric limits, supported functions, and product capabilities; mark unverified values as unknown.
04
Expected debrief: the matrix should show that Modbus RTU and TCP differ in transport/framing while Ethernet and RS-485 describe different connection layers.
SUGGESTED VISUAL
IMAGE SPACE
Insert the visual described in the speaker notes
COMMUNICATION LINKS AND PLC PROTOCOLS
15 / 18
Notes: Communication Links and PLC Protocols | Week 06 | LO2 Slide 15 of 18 | Suggested time: 20 minutes | Criteria: P3 TEACHING NOTES AND ACTIVITY CUES 1. Activity procedure: create two separate matrix sections, comparing a specified Ethernet/serial interface pair and Modbus TCP/RTU protocol variants; do not place protocol names in the physical-link column. 2. For each option record topology, distance constraints, noise/installation considerations, bandwidth/update suitability, typical PLC use, commissioning strengths, and limits. 3. Add one documented MedPack endpoint pair and cite official manuals for all numeric limits, supported functions, and product capabilities; mark unverified values as unknown. 4. Expected debrief: the matrix should show that Modbus RTU and TCP differ in transport/framing while Ethernet and RS-485 describe different connection layers. TEACHING VISUAL This slide has a reserved image bay. Add the image described below. OPTIONAL IMAGE PROMPT Original completed-looking but text-free comparison matrix layout beside a PLC Ethernet port and an RS-485 terminal, with visual icons for topology, noise, and use case.

## Slide 16
UNIT 5009 / WEEK 06 / LO2
20 MIN
P3
Draw and label an end-to-end connection
TEACHING POINTS
01
Procedure: draw the selected PLC, HMI or remote-I/O endpoint, every switch/gateway, physical medium/interface, protocol, endpoint roles, addressing, and one MedPack data path.
02
Label the protocol and the physical interface separately; show a PillCount read or StartRequest exchange with data type, direction, and the source manual/map.
03
Peer review test: another learner should be able to identify the cable/interface, protocol, endpoint configuration, data map, and one likely failure boundary without verbal hints.
04
Expected debrief: if the drawing says only “Ethernet” or “Modbus,” it is incomplete because it omits either the actual connection or the application exchange.
COMMUNICATION ARCHITECTURE
PLC
CONTROLLER
LOCAL I/O
REMOTE I/O
HMI
SCADA
Label the medium and protocol on every connection
COMMUNICATION LINKS AND PLC PROTOCOLS
16 / 18
Notes: Communication Links and PLC Protocols | Week 06 | LO2 Slide 16 of 18 | Suggested time: 20 minutes | Criteria: P3 TEACHING NOTES AND ACTIVITY CUES 1. Procedure: draw the selected PLC, HMI or remote-I/O endpoint, every switch/gateway, physical medium/interface, protocol, endpoint roles, addressing, and one MedPack data path. 2. Label the protocol and the physical interface separately; show a PillCount read or StartRequest exchange with data type, direction, and the source manual/map. 3. Peer review test: another learner should be able to identify the cable/interface, protocol, endpoint configuration, data map, and one likely failure boundary without verbal hints. 4. Expected debrief: if the drawing says only “Ethernet” or “Modbus,” it is incomplete because it omits either the actual connection or the application exchange. TEACHING VISUAL The slide uses an editable communication architecture diagram. Keep it unless the prompted image communicates the idea more clearly. OPTIONAL IMAGE PROMPT Original clear engineering network diagram with PLC, switch, HMI, cable types, endpoint roles, and a highlighted count-data path, with no text or labels.

## Slide 17
UNIT 5009 / WEEK 06 / LO2
7 MIN
P3
P3 common errors
TEACHING POINTS
01
Correct four frequent errors: calling RS-485 a protocol, treating Ethernet as an application protocol, assuming same cable means compatibility, and presenting a speed/distance as universal.
02
A complete comparison names the chosen medium/interface, topology, protocol, endpoint roles, relevant noise controls, and the source for product-specific limits.
03
Ask learners to repair one weak claim: “Ethernet is deterministic and all PLCs can connect” becomes a qualified statement tied to protocol, traffic design, compatible devices, and verified timing requirements.
FORMATIVE CHECK
01
PHYSICAL LINK
02
PROTOCOL
03
ENDPOINT MAP
04
SOURCE / LIMIT
COMMUNICATION LINKS AND PLC PROTOCOLS
17 / 18
Notes: Communication Links and PLC Protocols | Week 06 | LO2 Slide 17 of 18 | Suggested time: 7 minutes | Criteria: P3 TEACHING NOTES AND ACTIVITY CUES 1. Correct four frequent errors: calling RS-485 a protocol, treating Ethernet as an application protocol, assuming same cable means compatibility, and presenting a speed/distance as universal. 2. A complete comparison names the chosen medium/interface, topology, protocol, endpoint roles, relevant noise controls, and the source for product-specific limits. 3. Ask learners to repair one weak claim: “Ethernet is deterministic and all PLCs can connect” becomes a qualified statement tied to protocol, traffic design, compatible devices, and verified timing requirements. TEACHING VISUAL The slide uses an editable formative check diagram. Keep it unless the prompted image communicates the idea more clearly. OPTIONAL IMAGE PROMPT Original split visual contrasting an incorrect tangled PLC network sketch with a corrected layered topology drawing, using symbols only and no text.

## Slide 18
UNIT 5009 / WEEK 06 / LO2
8 MIN
P3
Exit ticket: compare, do not list
TEACHING POINTS
01
In a short response, compare one physical link/interface pair and one protocol pair on two dimensions from topology/distance, noise, speed/bandwidth, and typical use.
02
Include one MedPack use case and state one compatibility fact that must be verified in the selected PLC or HMI manual.
03
Expected answer distinguishes a connection (for example, RS-485) from a message/protocol (for example, Modbus RTU) and avoids unsupported universal numeric claims.
FORMATIVE CHECK
01
PHYSICAL LINK
02
PROTOCOL
03
ENDPOINT MAP
04
SOURCE / LIMIT
COMMUNICATION LINKS AND PLC PROTOCOLS
18 / 18
Notes: Communication Links and PLC Protocols | Week 06 | LO2 Slide 18 of 18 | Suggested time: 8 minutes | Criteria: P3 TEACHING NOTES AND ACTIVITY CUES 1. In a short response, compare one physical link/interface pair and one protocol pair on two dimensions from topology/distance, noise, speed/bandwidth, and typical use. 2. Include one MedPack use case and state one compatibility fact that must be verified in the selected PLC or HMI manual. 3. Expected answer distinguishes a connection (for example, RS-485) from a message/protocol (for example, Modbus RTU) and avoids unsupported universal numeric claims. TEACHING VISUAL The slide uses an editable formative check diagram. Keep it unless the prompted image communicates the idea more clearly. OPTIONAL IMAGE PROMPT Original exit-ticket still life showing a small PLC, two alternative communication cables, a protocol frame sketch, and a blank answer sheet; no writing or logos.